## Slide 1
Session I: Safety case approach
Safety Functions: Review
Jan Marivoet
SCK•CEN, Mol, Belgium
Final PAMINA Workshop Hohenkammer , 28-30 September 2009

## Slide 2: What are safety functions?
IAEA glossary (2007):
  “a specific purpose that must be accomplished for safety”
In a radioactive waste disposal context:
  “a function that the disposal system should fulfil to achieve long-term safety"

## Slide 3: Where are SFs coming from?
Safety functions were introduced around 1980 for safety studies of nuclear power plants
Defence-in-depth concept (IAEA, 1996): successive multi-barriers have to ensure the fulfilment of 3 basic safety functions:
  Controlling the power
  Cooling the fuel
  Confining radioactive material

## Slide 4: Why were SFs introduced for waste disposal?
Around 1995 the defence-in-depth concept was applied in Sweden to geological disposal systems
Limitations in the application of the multi-barriers concept in safety assessments:
  Gradual degradation of the barriers
  Several components / processes can contribute to a safety function
Helpful for communication

## Slide 5: SFs in regulations and guidelines (1)
International
  Safety Case Brochure (NEA, 2004)
    recommends the use of SFs for describing the contributions of the main system components
  Safety Standards for Geological Disposal (2006)
    “… post-closure safety is provided by means of multiple safety functions. That is, safety shall be provided by means of multiple barriers whose performance is achieved by diverse physical and chemical processes."

## Slide 6: SFs in regulations and guidelines (2)
National regulations
  Not explicitly used before 2000
    E.g., old French regulations (DSIN, 1991): “… protect the waste by limiting flow of water in contact with the waste and intrusive human actions, and limit and retard the transfer of radionuclides released by the waste to the biosphere”
  Explicitly used since 2002
    Sweden: SKI (2002)
    France: ASN (2008): “the safety functions of a disposal system are: limit water flow, confine radioactivity, isolate the waste from man and the biosphere”
    Germany: BMU (draft 2008)

## Slide 7: Safety functions
Waste management strategy for HLW
  Concentrate and contain (C&C) the waste
    in contrast to a “disperse and dilute” (D&D) strategy
Safety functions
  Stability/isolation
  Containment
  Limited and delayed releases

## Slide 8: Stability/isolation
Isolate the waste and EBS from surface events and climate changes
Reduce probability of human intrusion
Thick geological formations overlying the host formation
Stability of the region in which the repository site is located

## Slide 9: Containment
  Called “isolation” by SKB and POSIVA
HLW is contained in a long-lived container (or salt formation) that prevents groundwater from coming in contact with the disposed waste
Metallic container: Cu canister, C-steel overpack
Host salt formation

## Slide 10: Limited and delayed releases
This SF becomes active after failure of the containment SF
Delay releases into biosphere to make use as much as possible of radioactive decay
Spread releases to limit the amounts of radionuclides that are released per year into the biosphere

## Slide 11: Limited and delayed releases: Sub-safety functions (ONDRAF/NIRAS)
Limit releases
  Waste matrix, solubility limits
Limit water flow
  Low hydraulic conductivity of bentonite backfill or clay of host formation
  Absence of water in salt dome/layer
Retardation
  Absence of advective transport
  Sorption on materials of NF or host formation

## Slide 12: Dilution
Dilution plays a role in the estimation of doses
Dilution is not considered as a safety function
  Cannot be controlled by design and only partially by site selection
  Is expected to change with time
  Optimising dilution (D&D) can conflict with the C&C waste management strategy for HLW

## Slide 13: Ensuring that the SFs will be available
SKB
  Safety function indicators
    understanding the properties of the component
    quantitative criteria
ONDRAF/NIRAS
  Tree of safety claims/statements
    Underpin the SF → substantiation from the assessment basis
ANDRA
  Functional analysis
    Subfunctions → requirements

## Slide 14: Applications (1)
Determination of the safety strategy
  ONDRAF/NIRAS, Andra, SKB, and Nagra
Developing the repository concept
  ONDRAF/NIRAS, NRI/RAWRA, Andra, SKB, and POSIVA
Analysis of the functioning of the repository system
  ONDRAF/NIRAS, Andra, SKB, NRI/RAWRA, POSIVA, and NDA
Testing the robustness of the repository system
  Andra and GRS-Cologne

## Slide 15: Applications (2)
Structuring the safety case (assessment basis)
  ONDRAF/NIRAS, Andra, Nagra, SKB
Scenario identification
  ONDRAF/NIRAS, SKB, Andra, GRS-Cologne
Uncertainty analyses
  Andra
Identification of performance indicators
  (SPIN project), ONDRAF/NIRAS, Andra, NRI/RAWRA, Nagra, GRS-Braunschweig
Communication
  ONDRAF/NIRAS, SKB, Nagra, Enresa, NRI/RAWRA

## Slide 16: Safety concept
Used for
Safety strategy
Functional analysis
  Components
  Repository concept
Testing robustness

## Slide 17: Scenario development (cf. Session II: Scenarios)
Scenario identification
Uncertainties that can affect a SF
Grouping of altered scenarios
Deriving “what-if” scenarios

## Slide 18: Performance indicators of safety functions (cf. Session IV: Indicators)

## Slide 19: Communication
Internal
  Safety concept based on SFs is used for interaction between the 3 main groups involved in the development of a safety case: engineers developing the repository design – scientists of the assessment basis – safety assessors
External
  SFs help to explain the functioning of a geological disposal system in easily understandable terms to non-technical audiences

## Slide 20: Conclusions
Application of defence-in-depth principle led to the introduction of safety functions for geological disposal systems around 1995
SFs are intensively used and play an important role in many Safety Cases since 2000
Strong similarity in the sets of SFs derived in various national RWM programmes
Safety demonstration of geological disposal systems is shifting from a component-based to a safety-function-based reasoning
Various applications of SFs in recent Safety Cases