## Slide 1
Safety strategy – Review
Manuel Capouet
With the contribution of Daniel Galson
PAMINA Final Workshop (Hohenkammer, September 2009)
Notes: <number>

## Slide 2
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Contributors
Notes: <number>

## Slide 3: Outline
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
International background
Safety strategy general points
Safety strategy specific points
  Management strategy
  Siting and design strategy
  Assessment strategy
Summary conclusions

## Slide 4: Starting point: The post-closure safety case for a geological repository (NEA 2004)
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
The safety strategy is the high-level approach adopted for achieving safe disposal, and includes a management strategy, a siting and design strategy, and an assessment strategy
  Management strategies include maintaining sufficient flexibility within a step-wise planning and implementation process to cope with unexpected site features or technical difficulties and uncertainties that may be encountered, as well as to take advantage of advances in scientific understanding and engineering techniques
  The siting and design strategy is generally based on principles that favour robustness and minimise uncertainty, including the use of the multi-barrier concept
  The assessment strategy must ensure that safety assessments capture, describe and analyse uncertainties that are relevant to safety, and investigate their effects
Notes: <number>

## Slide 5
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
strategy
Management
strategy
Intrinsic quality of the site and design
Compliance with dose and risk criteria (incl. reliability of the
analyses)
Safety indicators complementary to dose and/or risk
Adequacy of the strategy to manage uncertainties and open questi
ons
Strength of geological disposal as a waste management option
Safety case at a given stage in disposal system
planning and development
Purpose and context of the safety case
Safety strategy
Assessment basis
Evidence, analyses and arguments
Synthesis
System concept
Methods, models, computer codes and database
Scientific and technical information and understanding
Siting and design
strategy
Assessment
strategy
Management
strategy
Intrinsic quality of the site and design
Compliance
with
dose
and
risk
criteria
(
incl
.
Reliability
of
the
analyses)
Safety
indicators
complementary
to dose
and
/or
risk
Adequacy
of
the
strategy
to manage
uncertainties
and
open questions
Strength
of
geological
disposal
as a
waste
management option
Key findings and statement of confidence
vis
-
à
-
vis
purpose and context
Relationships between the different elements of a safety case
Notes: <number>

## Slide 6: Safety strategy: iteration
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
NDA approach
The safety strategy is the high-level iterative and stepwise approach adopted for achieving safe disposal [All]
ANDRA approach
Notes: <number>

## Slide 7: Safety strategy: Safety functions
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Multiple safety functions: core element of the safety strategy for all programmes
Play a major role in:
  Developing the repository concept
  Assessment strategy, e.g. approach to scenario derivation and uncertainty analysis
  Determining and structuring the safety strategy, e.g. by setting priorities in R&D programmes

## Slide 8: Safety strategy: Integrated approach
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Some organisations [POSIVA, Ondraf/Niras SCK•CEN, GRS-K] have extended the concept of multiple safety functions into a “safety concept” integrating siting and design principles, specific features of the disposal system, and management processes
Posiva example

## Slide 9: Safety strategy: Safety timescales
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Figure 13 - Illustration of the main features of the expected evolution of a repository in the case of heat-emitting wates.
Ondraf/Niras example
The use of safety functions to guide safety strategy over safety-relevant timescales

## Slide 10: Management strategy: Main elements
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
The synthesis of the results of safety assessment and other tasks involved in the safety case is the remit of a specific Core Group [POSIVA, ANDRA]
The scientific teams evolved to an approach centred on the major phenomena controlling repository evolution [ANDRA]
The role of safety management is to improve the safety of the repository in a continuous process and to promote a safety culture [GRS-K]… includes:
  A staged approach to demonstrate safety (constrained optimisation)
  Four implementation stages: above-ground site investigation, underground site investigation, planning and construction, operation and closure
As the programme evolves, project interactions increase in intensity and frequency => transparent and traceable communication is essential [All]
Necessity of preparing a detailed roadmap indentifying clear milestones and decision points [ENRESA, NDA, IRSN]…
  including early discussion with regulators and other stakeholders [ENRESA, NDA]
Notes: <number>

## Slide 11: Management strategy: QA
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Confidence in a safety case rests on systematic and well-defined QA programme
QA purposes:
  To provide traceability and transparency of the work flow within the organisations [POSIVA, Andra, NDA]
  To ensure traceability and transparency of the data, models and documentation [ENRESA]
    A hierarchical database that will be developed over many decades
  To ensure that the models used are fit for purpose (qualification, verification, validation) [All]
  To ensure completeness of the knowledge used in a safety case (peer review, FEP checks)
Notes: <number>

## Slide 12: Siting & design strategy: Guiding principles
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Multiple safety functions
  Post-closure safety shall be provided by means of multiple barriers or safety functions
  The overall performance of the geological disposal system shall not be unduly dependent on a single barrier or safety function
Robust systems
  A lack of complex, poorly understood or difficult to characterise features or phenomena
  Ease of quality control
  The absence of - or relative insensitivity to - detrimental phenomena arising within the disposal system, or externally (geological and climatic phenomena)
  The absence of - or relative insensitivity to - uncertainties with the potential to compromise safety
Notes: <number>

## Slide 13: Siting & design strategy: Demonstrability
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Demonstrability is a major principle in safety case development
  A disposal facility is “demonstrated” if the design is shown to be simple, technically feasible and robust [Andra, IRSN, FANC/Bel V, Ondraf/Niras SCK•CEN]
  A safety case is “demonstrated” if it contains multiple lines of arguments and analyses for safety of the disposal system [GRS]
  Safety demonstration requires a justified programme of studies [IRSN] - the programme must define:
    The main safety demonstration issues in each stage of disposal system development
    The information requirements of the safety assessment approach
    Monitoring requirements during the different phases of disposal facility development
Notes: <number>

## Slide 14: Siting & design strategy: Siting principles
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Siting principles seek to minimise the likelihood of inadvertent human intrusion, while maximising geological stability of the host rock and physical and chemical features favouring waste containment
  Siting should not compromise the future use of natural resources, and should focus on areas of relatively low population density [POSIVA, ENRESA, FANC/Bel V]
  Siting should consider the characteristics of the host rock [Andra, ENRESA, FANC/Bel V]
Use of voluntarism and partnership approaches in siting means that socio-economic issues and community willingness to participate are increasingly important!
Notes: <number>

## Slide 15: Siting & design strategy: Feasibility
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
Design feasibility is guided by:
  Technology availability
  Technology ease of implementation
  Reversibility and monitoring choices
  [Andra, IRSN]
IRSN: “The definition of a ‘reversible’ repository needs however to be clarified and requires to be possibly agreed upon at international level.”
Notes: <number>

## Slide 16: Safety assessment strategy: international guidance
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
safety functions
safety statements
Siting and design principles
safety concepts
regulatory requirements
storyboards,
situations,
matrices
FEP
international
List
Notes: <number>

## Slide 17: Safety strategy: Conclusions
PAMINA Final Workshop (Hohenkammer, September 2009)
<number>
The safety strategy is the high-level iterative and stepwise approach for achieving safe disposal
  The management strategy relies on focused and interacting teams governed by appropriate QA procedures
  The siting and design strategy relies on a robust system of multiple safety functions playing a major role in the development of the repository concept, in safety assessment, and in setting priorities for R&D programmes
  The safety assessment strategy is consistent with the IAEA ISAM safety assessment methodology. Increased use of structuring elements to communicate safety assessments
Notes: <number>