## Slide 1
Final Workshop
Workshop in Hohenkammer, Germany
September, 28. - 30. 2009
Session II: Evolution of the disposal system
Subject : Human Intrusion - Review
Thomas Beuth
Notes: <number>

## Slide 2: Content
<number>
General Information and Aspects
Regulations and Guidelines
Terminology
Methodology
Conclusions
Notes: <number>

## Slide 3: General Information and Aspects
Main goal was to summarise the essential facts, aspects, and views and to identify common opinions and understanding, different views, gaps etc.
List of participating Organisations which provide a contribution
<number>
Acronym | Organisation | Country
ANDRA, IRSN1) | Agence Nationale pour la Gestion des Déchets Radioactifs, Institute de Radioprotection et de Sureté Nucléaire | France
ENRESA | Empresa Nacional de Residuos Radioactivos S.A. | Spain
FANC, BEL V2) | Federaal Agentschap voor Nucleaire Controle, BEL V | Belgium
GRS-BS | Gesellschaft für Anlagen- und Reaktorsicherheit mbH (Braunschweig) | Germany
GRS-K | Gesellschaft für Anlagen- und Reaktorsicherheit mbH (Köln) | Germany
NDA | Nuclear Decommissioning Authority | United Kingdom
NRG | Nuclear Research & Consultancy Group | Netherlands
NRI | Nuclear Research Institute Rez plc. | Czech Republic
POSIVA | Posiva Oy | Finland
SCKCEN, ONDRAF/ NIRAS3) | Studiecentrum voor Kernenergie - Centre d'Etude de l'Energie Nucléaire/ Nationale Instelling voor Radioactief afval en verrijkte splijtstoffen | Belgium
1) IRSN follows Andra's explanations regarding the regulatory aspects.
2) BEL V follows FANC's explanations.
3) Joint contribution from SCK·CEN and ONDRAF/ NIRAS
Notes: <number>

## Slide 4: General Information and Aspects (cont.)
Classification of “Human Intrusion” (HI)
<number>
Key issues in terms of HI
  predictability;
  general assumptions and conditions;
  measures against HI;
  types of HI actions and scenarios;
  anomalies and noticeable features;
  exposed groups, doses and risks and evaluation of consequences.
Notes: <number>

## Slide 5: Regulations and Guidelines
Main observations from the review
  Regulations and guidelines refer to HI in relation to the disposal of high active waste in deep geological formations.
  All in all four of the participating countries have regulations or guidelines in place (Czech Republic, Finland, France, and UK).
  The existing regulation in Germany (at that time) include no specific regulatory requirements for HI. (German safety requirements => are now on-hand).
  Other participating countries have no regulatory requirements or provisions that directly relate to the topic of HI (Netherlands, Spain).
Outcome from the WS
  HI should be part of regulations and guidelines provided by the responsible authorities (framework, scope of the investigations, constraints and conditions).
  Relevant actions e.g. drilling, mining for HI scenarios should also be provided.
  It should be acknowledged that selected HI scenarios can never be complete or comprehensive.
  HI scenarios should be determined on a stylised basis, since a systematic development of HI is not possible.
  HI has to be considered in the site selection process and in the design phase of a repository.
<number>
Notes: <number>

## Slide 6: Terminology
<< A human action affecting repository integrity and potentially having radiological consequences is known as human intrusion. >> [ICRP, 1998]
<< ... by definition, an intrusion event bypasses some or all of the barriers that have been put in place as part of the optimisation of protection. >> [ICRP, 1998]
<< Future human actions of concern are those occurring after repository closure that have the potential to disrupt or impair significantly the ability of the natural or engineered barriers to contain the radioactive wastes. >> [NEA, 1995]
<< Human action causing partial or full degradation of one of several safety barriers of the disposal system, and that may expose the author of the intrusion (named as “the intruder”) or the surrounding population to a radiological risk. >> [FANC]
<< ... inadvertent action that has the potential to disrupt or impair significantly the ability of the natural or engineered barriers to contain radioactive waste >> [SCK•CEN, ONDRAF/NIRAS]
<< Human intrusion (HI) is understood as any human activity following the closure of the repository mine that will directly damage the barriers within the backfilled and sealed mine workings and the isolating rock zone >> [GRS-K]
Résumé
  It should be pointed out that the above listed definitions of both national and international organisations are rather different in terms of the wording. However, the general statement that human actions involve a direct damaging of barriers is more or less the same.
<number>
Notes: <number>

## Slide 7: Terminology (cont.)
Main observations from the review
  Only few contributions provide a definition for “Human Intrusion”
  Some deliver no definitions, neither for “Human Intrusion" nor for other related terms
  Some refer to definitions from other organisations and reports respectively (ICRP, NEA)
  Many additional terms and synonyms in connection with human actions were used
Outcome from the WS
  As a result of the workshop the participants agreed on the following description: HI can be understood as human actions which have the potential to directly jeopardise the isolating capacity of the barriers of the disposal system and therefore might have radiological consequences.
  It was also agreed by the participants to adopt the definitions given by the NEA regarding other terms associated with HI:
    Unintended actions: << Those in which either the repository or its barrier system are accidently penetrated or their performance impaired, because the repository location is unknown, its purpose is forgotten, or the consequences of the actions are unknown. >> [NEA, 1995]
    Intentional actions: << In contrast, if future intruders are aware of the waste and the consequences of disturbing the repository or its barrier system, then their actions are intentional. >> [NEA, 1995]
<number>
Notes: <number>

## Slide 8: Methodology: Predictability of HI
Examples
  << The representation of future human behaviour in assessment models is necessarily stylized, as it is not possible to predict behaviour in the future with any certainty. >> [IAEA, 2006]
  << The prediction of future human actions is fraught with uncertainty >> [NEA, 1995]
  << ...there is little or no scientific basis for predicting the nature or probability of future human actions... >> [ICRP, 1998]
  << …we conclude that there is no technical basis for predicting either the nature or the frequency of occurrence of intrusions. >> [NAS, 1995]
  << Given the impossibility to predict future human actions and technologies, the assessment of the impact of human intrusion will be made by means of arbitrary stylized scenarios. >> [FANC]
  << ...the evolution, way of life, and behaviour of the society, inclusive human intrusion, cannot be predicted over time frames, which have to be considered for the isolation period of radioactive wastes. >> [GRS-K]
  << Assessments of the post-closure safety of a repository typically extend over periods of hundreds-of-thousands of years. Over this period of time, the form of human society will change in a manner that cannot be predicted. >> [NDA]
Outcome of the WS
  HI cannot be predicted over timescales which are relevant or of interest for the disposal of high active waste.
<number>
Notes: <number>

## Slide 9: Methodology: General assumptions and conditions
HI cannot be ruled out
It is not possible to derive occurrence probabilities for HI
HI cannot be developed systematically
HI scenarios should be treated separately from the other scenarios
Stylised HI scenarios should be provided
Today´s technology and practice should be assumed
<number>
Notes: <number>

## Slide 10: Methodology: Measures against HI
General statements
  Measures against HI are limited
  Effectiveness of specific measures should be evaluated
  Measures must not compromise the safety; measures should not counteract each other
Discussed measures
  Avoiding resources => some reservations
  Depth of the repository => seen as one of the most appropriate measures
  Institutional control => seems to be appropriate, task of the regulator
  Information preservation => seen as an appropriate measures, short term
  Other measures (marker, monument) => no statement, task of the regulator
<number>
Notes: <number>

## Slide 11: Methodology: Types of human actions as a basis for scenarios
The range of motivations and techniques include:
  drilling and operation of a borehole
    exploration,
    exploitation of resources e.g. oil, gas, minerals,
    extraction e.g. of groundwater, geothermal energy
    injection e.g. liquids and gases
  construction and operation of a mine at the site or in the vicinity
    excavation, solution
    solution mining e.g. minerals,
    conventional mining e.g. coal, ores, other minerals
    utilisation e.g. storage and disposal of substances
  construction and operation of a cavern
    excavation, solution
    leaching e.g. salt
    utilisation e.g. storage and disposal of liquids and gases
Outcome of the WS:
  The main actions for HI events are drilling and mining, whereas the main purposes are exploration of the site, exploitation and extraction of natural resources and injection of substances and/ or resources for storage and disposal. These topics take into account the assumption that HI should be considered in the view of today´s available technology and habits of the society. It was also concluded that exploratory drilling is actually the initial event for all the other actions like mining and exploitation.
<number>
Notes: <number>

## Slide 12: Methodology: Anomalies and noticeable features
Some indications of the existence of waste and repository characteristics are:
  Differences of porosity, permeability and density in consequence of mining activities and backfilling of e.g. bentonite, crushed salt.
  Differences in temperature of such disposal areas caused by heat generating wastes.
  Emplacement of dissimilar material into the underground such as waste containers, canisters, casings, concrete, radioactive waste etc.
  Ionising radiation, radiotoxicity
There are few examples from the contributors that discuss the possible detection of the disposal system and the associated hazard
  drillings and excavations are preceded by airborne and ground-based geophysical investigations, by which the repository will be detected (POSIVA)
  construction of a DS leaves underground tracks due to mining and waste (GRS-K)
  drilling team should become aware of the presence of exotic materials in the cuttings (SCK•CEN, ONDRAF/NIRAS)
Outcome of the WS:
  The investigation of HI scenarios should also include the discussion if the anomalies induced by the waste and the repository could be detected based on today´s knowledge and applied technology.
<number>
Notes: <number>

## Slide 13: Methodology: Exposed groups, doses and risks and evaluation of consequences
Outcome of the WS:
  There are actually two types of exposed groups in the case of HI events:
    Group of intruders which might receive immediate or direct consequences;
    group of people (residents, public) which might receive direct and indirect consequences).
  Due to the widely varying underlying assumptions for HI scenarios, the radiological consequences can vary greatly.
  The investigation of HI scenarios should be undertaken in a more qualitative manner.
  Calculated doses should not be measured against radiological thresholds.
  There might be some cases that allow the developer to treat the HI scenario like a common alternative scenario, e.g. release of radionuclides via groundwater path.
  Finally, it was stated that the consequences should be more seen as indicators which give information about the resilience and robustness of the disposal system.
<number>
Notes: <number>

## Slide 14: Conclusions
Regulations:
  broad consensus about the need of regulations for the treatment of HI in the SC
  scenarios should be determined on a stylised basis (can never be complete or comprehensive)
  HI should be considered in the site selection process and in the design phase of a repository.
Terminology:
  HI can be understood as human actions which have the potential to directly jeopardise the isolating capacity of the barriers of the disposal system and therefore might have radiological consequences
  other terms were accepted according to provided definitions from the OECD/NEA
Methodology:
  HI cannot be predicted, it is not possible to derive HI scenarios in a systematic way
  current knowledge and technology have to be taken into account
  only unintended HI have to be considered
  appropriate measures against HI are limited (sufficient depth, information preservation, institutional control)
  main types of actions are drilling and mining (exploratory drilling is actually the initial event)
  investigation, if the anomalies induced by the waste and the repository can be detected
  investigation of HI scenarios should be undertaken in a more qualitative manner
  calculated doses should not be measured against radiological thresholds
  consequences should be more seen as indicators
<number>
Notes: <number>