## Slide 1
WP1.1
Topic 9. Biosphere - Review

## Slide 2: General presentation
Eight programmes at different stages of development:
  Ranging from generic studies as a preliminary phase to site selection, to highly sophisticated site-specific landscape models of the evolving surface environment at particular sites.
International guidance and directives (ICRP, Euratom, IAEA, NEA):
  Interpretation of those guidance and directives provides the basis for regulation at the national level.
National regulatory framework:
  For most countries, guidance is under process.
  In some countries, regulations specify parameters for use in biosphere modelling and require that organ doses be evaluated, as well as whole body effective dose equivalents.

## Slide 3: Common approaches and tendencies
All the operators consider:
  A dose limit, or constraint, specified in most countries to ensure that radiological protection criteria are met (from 0.1 to 0.3 mSv/year, risk),
  At long timeframes, calculated dose is more suitable for qualitative evaluation of results and sensitivity analyses to some parameters,
  The consideration for climate evolution in addition to the definition of a today reference biosphere by a set of additional possible biospheres in the future and sensitivity analysis,
  The definition of multiple exposure pathways,
  The definition of food consumption and diet consistent with today habits and database,
  The identification of radionuclides to be modeled with specific models,
  The identification of a need for further consideration of potential impacts on non-human biota, and a focus on assessment of health effects.

## Slide 4: Highlighting some common aspects
Dose constraints and timescale/situation dependency:
  End point of safety assessment calculations is a numerical value that can be compared to the regulatory requirements (up to 0.3 mSv/year).
  Calculated dose is the cumulative value from multiple exposure routes.
  For long-term, dose should be interpreted as an illustrative measure of system performance (completed with other safety indicators).
  Annual individual dose may be used as a performance measure, but considering the likelihood of the initiating event occurring (high-consequence/low-probability scenarios). Risk approach.

## Slide 5: Highlighting some common aspects
Assumption of present-day conditions and consideration of climate-change scenarios:
  Present-day biosphere considered as the basis for the description of the biosphere (including predictable changes in the environment).
  Study of the past and current environments to develop representative biosphere states from analogue sites and consideration of the future impact of greenhouse effects and other human activities.
  Description of the human habits (similar to those of the present-day population).
  Some organizations use average food consumption rates, but assume that all food consumed comes from the most contaminated parts of the environment – self-sustaining farming group.
  Future climate states based on analogue conditions take their exposed groups and food consumption rates from analogue sites.

## Slide 6: Highlighting some common aspects
The exposure mechanisms considered:
  Multiple exposure pathways are generally studied but those selected depend on the exact nature of the hydrogeological and climatic environment on the disposal as well as on human habits (ICRP 101).
  Conversion to dose via these pathways is facilitated by a set of Dose Coefficients documented by ICRP 60.
  For one organisation, release from the geosphere is input directly to the biosphere model and the resulting time-history of dose contains the dynamics of the release from the geosphere and the biosphere.
  In agreement with ICRP 101, some approaches consist of exploring the different transfer pathway of the site and region and not exclude a priori some transfer pathway.

## Slide 7: Differences
Exposed groups:
  Wide range in the level of prescription and advice provided in regulation with regard to biosphere modelling and the consideration of exposed groups.
Age groups considered:
  For most organisations, adults are the age group considered in the assessment, and it is implicit that the adult dose can be used as a measure of lifetime exposure.
  Doses calculated to different age groups (infants, adults). ICRP 81 recommends 6 age groups.

## Slide 8: Ongoing developments
Use of radionuclide-specific biosphere models:
  A single generic modeling framework is used for all the radionuclides.
  In some countries, 14C and 36Cl (but also 79Se, 129I and 3H), are treated with radionuclide-specific models.
  Some countries suggest that modeling could consider the influence of transitory climate conditions on the geosphere-biosphere interface.
Non-human biota:
  EC projects FASSET, ERICA and PROTECT are cited as the basis for this aspect of the biosphere.
Health effects:
  Only radiological health effects have so far mainly been considered in safety assessment calculations. Some organisations are starting to consider potential health effects associated with chemical toxicity.

## Slide 9: Conclusions
Stage reached in the disposal programme:
  Following a staged approach, organisations are progressing towards more detailed models, as more information becomes available.
Common comments from implementers:
  An iterative approach and a good working relationship between regulators and the developer are essential to facilitate development of the safety case in a manner acceptable to regulators.
  There could be benefit in an improved glossary of terms.
Better justify:
  Age groups and exposed groups.
  How are low-probability scenarios dealt with by countries using risk approach ?
Harmonization of the approach ?
  Facilitate the comprehension of the stakeholders.
  Consistency when discussing with public.