## Slide 1
  Analysis of the evolution of the repository system
PAMINA
WP1.1 Comprehensive review of methodologies
Prepared by Lise Griffault
Task Leader
Notes: <number>

## Slide 2
Group 1
1. Safety functions
2. Definition and assessment of scenarios)
3. Safety indicators and performance/function indicators
4. Uncertainty management and uncertainty analysis
Group 2
5. The assessment strategy / The safety approach
6. Analysis of the evolution of the repository system
7. Modelling strategy
8. Sensitivity analysis
Group 3
9. Human intrusion
10. Biosphere
11. Criteria for input and data selection
WP 1.1 Comprehensive Review of Methodologies and Approaches in the Safety Case

## Slide 3
Acronym | Organisation | Country | Contributions
ANDRA | Agence Nationale pour la Gestion des Déchets Radioactifs | France | X
AVN | Association Vinçotte Nuclear | Belgium | 
BGR | Bundesanstalt für Geowissenschaften | Germany | 
ENRESA | Empresa Nacional de Residuos Radioactivos S.A. | Spain | X
GRS-K* | Gesellschaft für Anlagen- und Reaktorsicherheit mbH | Germany | X
IRSN* | Institute de Radioprotection et de Sureté Nucléaire | France | X
NDA | Nuclear Decommissioning Authority | United Kingdom | X
NRG | Nuclear Research & Consultancy Group | Netherlands | X
NRI, RAWRA | Nuclear Research Institute Rez plc., Radioactive Waste Repository Authority | Czech Republic | X
POSIVA | Posiva Oy | Finland | X
SCKCEN, ONDRAF/ NIRAS | Studiecentrum voor Kernenergie - Centre d'Etude de l'Energie Nucléaire/ Nationale Instelling voor Radioactief afval en verrijkte splijtstoffen | Belgium | X
EWG: Evaluator working group
DWG: Developer working group
Two contributions from EWG
Seven contributions from DWG

## Slide 4
Definition

## Slide 5
  Stipulate dose and/or risk values to conform to
  No specific regulatory requirements for analysis of the evolution of the repository system
    but necessity to show understanding of the disposal system evolution is acknowledged
  Detailed requirements and expectation related to repository evolution
    To justify (or show) a good understanding of the processes having influences on the evolution of the repository system
    Account for the factors, activities and processes of each phases (including during operational) which might have an influence on the long term safety of the repository
    Natural effects (endogenous and exogenous) and human induced effects,
    Account for disturbances induced by the repository (THMC, gas …)
  To define (and model) the spectrum of potential evolutions of the repository system (reference and altered evolution scenarios)
Regulatory Requirements

## Slide 6
Some national specificities
      Recommendations of timeframes to be considered
  Recommendations to account for a series of specific FEPs in scenarios (including human actions)
  Recommendations to model the evolutions of the system for representatives scenarios to evaluate the impact on man and the environment
  Recommendations to evaluate of the performance of the system
    ex: to show good performance of components contributing to safety functions
  May require specific methods such as “probabilities” in order to distinguish the possible repository evolutions or scenarios
    ex: to assess the occurrence probability of relevant factors playing an important role
Requirements and expectations

## Slide 7
To support safety analysis
  Safety analyses relies upon a thorough knowledge and understanding of processes and phenomena likely to evolve in the repository
To aim at the identification, analysis and conceptualisation of FEPs
  Obtain relevant FEPs to consider
  Analyse the FEPs (including the associated uncertainties)
  Organisation of FEPs (according to space and time)
To be a background for definition and assessment of scenarios
  Uncertainties analyses (qualitative safety analyses or quantitative)
  Scenario development (reference and altered):
    Which (THMCR-G) effects or FEPs can affect the safety functions, or the “barrier”
    How FEPs and uncertainties can affect the evolution of the disposal system
  Assessment of scenarios (quantification, compliance to regulatory requirements, performance of safety functions)
To provide information for design studies
  Design solutions (material and their evolution, architecture)
Place of the analysis of the evolution of the repository system

## Slide 8
  Generic probabilistic safety analysis (PROSA)
    International data base of FEPs
    Organisation of the FEPs (probabilistic analysis)
    Derivation of scenarios
  Phenomenological Analysis of Repository situations (PARS), “Storyboard”
    Identification of FEPs (usually from an acquisition program)
    Analysis and conceptualisation of FEPs (with associated uncertainties)
    Then derivation of scenarios (QSA, SEN, SEA)
  Well supported detailed modelling
    International data base
    Scenario definition cases
    Creation of conceptual model based on analysis of FEPs within a scenario
  All are a stepwise/iterative process
Approaches to analysis of the evolution of the disposal systems

## Slide 9
  Approaches consider
  Study of THMCR-Gas processes induced by the repository and their interactions
  Study of external FEPs (including human action)
  An iterative process : identification and analyses of FEPs evolve with the maturity of the project
  Account for evolution with time considering potential climatic changes
  International FEPs database
    Usually adapted to be relevant to the type of host rock
  Identification of FEPs
  Development of “site” or “disposal system” specific FEPs database
  from a large acquisition program
  (e.g. borehole, experimentations in underground research laboratory,…)
  International database is used for comparison (“checklist”)
Identification of FEPs

## Slide 10
  Description of the thermal, hydrological, mechanical, (bio) (geo) chemical and gas induced processes that can affect each of the system components
  Waste, canister, buffer, backfill, seals, host rock, geosphere, biosphere
Description of interactions between major disposal system components
  Coupling of processes (THMC) are to be studied
  Description of the evolution of the disposal system can distinguish
  The evolution of the near field
    ex: to account for coupling of THMC processes
  Evolution of the far field
    ex: to account for specific FEPs (glaciations)
  Evolution of the biosphere
    ex: to account for climatic evolution (different type of biosphere)
Description of FEPs

## Slide 11
    Several methods for analysis and conceptualization/representation of FEPs
    PROSA Generic probabilistic safety analysis
      A structured FEP Analyses methods which uses national/international database
    PARS Phenomenological Analysis of Repository situations
      A space-time description of the various phenomena affecting the repository's components and its environment.
      Site and concept specific FEPs (associated to an acquisition program)
    Storyboard diagrams
      Illustrated by a series of diagrams,
      Site and concept specific FEPs (associated to an acquisition program)
    Well supported detailed modeling
Analysis and conceptualization of FEPs

## Slide 12
The PROSA methodology was developed for the determination of scenarios
    Structured FEP Analyses method which uses national/international database
Choice of representative scenarios
  Assumption of a multi-barrier system (4: EBS, Salt, overburden and biosphere)
  Evolution can be characterized by the state of each barrier : present or by-passed
  For each barrier state: a number of FEPs from the database describing the state of the barrier
  They are the Primary FEPs : used to define the scenarios
Barrier and FEPs used in scenario development
  Collection of the FEPs that might influence the efficiency of the barrier
  Description of so called conceptual model : basis for estimating the occurrence probabilities of FEPs
  Account for geology, climate or human operations
EX: PROSA Generic probabilistic safety analysis (1/2)

## Slide 13
Classification of FEPs
  Primary FEPs : describe boundary conditions of the system and FEPs that describing transport causing processes
  Secondary FEPs: Transport FEPs : describe the transport of radioactivity through a barrier
  Variant FEPs : determine the rate of a Transport or a Primary FEP
  Other FEP : Variant FEPs with negligible influence in the scenario and excluded Primary FEPs which are not active in the scenario
Ex: PROSA Generic probabilistic safety analysis (2/2)
FEP representation table

## Slide 14
    PARS: A space-time description of the various phenomena affecting the repository's components and its environment
Breakdown of the repository into situations
  A “situation” corresponds to the phenomenological state of a component as part of the repository or of its environment during a given period of time
  Each corresponds to a space and time interval within which a few major phenomena dominate the evolution of the components
  Spatial fractioning according to the main repository components
  Each situation of the repository depends on the former situation
For each situation
  Detailed description of the components
  Identification of the major processes (Thermal, hydraulic, mechanical, chemical and radiological phenomena occurring and their coupling)
    site and concept specific FEPs (associated to an acquisition program)
  Determination of the associated uncertainties
PARS Phenomenological Analysis of Repository situations

## Slide 15
General Table of situations identified in PARS of Dossier 2005.
Andra – PARS Methodology

## Slide 16
PARS
A space-time description of the various phenomena affecting the repository's components and its environment.
Notes: <number>

## Slide 17
    An input for design studies
    An input for scenario derivation (normal evolution and altered evolution)
      QSA: analyses of uncertainties to derive scenarios SEN and SEA
        to define which effects (THMC-Geochemistry) can affect the functions
        to identify if uncertainties (of all types) or external events are taken into account:
      By design
      If not, in the definition of scenarios:
        In the normal evolution scenario (including sensitivity studies)
        Or in the altered evolution scenarios
      Not a probabilistic approach
        A qualitative evaluation of the likelihood of events, not quantitative
    An input data for modelling and digital simulation
        Assessment of the performance of safety function
        Assessment of the radiological impact
    PARS to support safety analysis including derivation of scenarios

## Slide 18
A series of diagrams, called “storyboard” representing the transverse and longitudinal cross section of a disposal tunnel:
        To structure the analysis of the plethora of processes taking place, the expected evolution of the EBS has been divided in key time sequences and in classes of processes (thermal, mechanical, hydraulic and chemical).
Each time sequence corresponds to a state of the repository characterized by key processes and events.
Figure 5 - Longitudinal cross section through the disposal tunnel showing key processes occurring approximately 10,000 years after emplacement
Figure 4. -Transverse cross section through the disposal tunnel showing key processes occurring approximately 10,000 years after emplacement
Storyboard diagrams, an illustration of the successive stages in the evolution

## Slide 19
    a basis for a further study of the THMC coupled processes
  ex: in SFC1 in complement to the findings of the experiment PRACLAY currently in progress.
an input for derivation of the reference and altered scenarios
  from a systematic evaluation of the uncertainties associated to the substantiations of the safety statements.
  safety statement: the broad expected evolution of the mean features of the system concept is primarily based on the efficient functioning of the safety functions
Storyboard diagrams, Derivation of Scenarios

## Slide 20
    Well supported detailed modeling
      Identification of relevant FEPs during the scenario definition phase of the safety case
      description of the system focuses on key properties of the barriers contributing to safety (ex: swelling capability of bentonite)
      creation of conceptual models for different parts of the repository
      Translation into mathematical models allowing predictions
Well supported detailed modeling
Temperature at different locations in bentonite and granite (ENRESA).

## Slide 21
Conclusions 1/4

## Slide 22
Conclusions 2/4
    Analysis for repository evolution
    Account for regulatory requirement when available
      To justify or show a good understanding of processes having influences on the disposal system
      to identify potential evolutions of the disposal system
    But some specificity
      to consider specific FEPs or scenarios
      to conform to dose and/or risk values
      to assess the occurrence probability of relevant factors playing an important role
      to assess the performance of the disposal system (ex: performance of components contributing to safety functions)

## Slide 23
    Approaches for identification, analysis and conceptualization of FEPs
      Generic probabilistic safety analysis (PROSA)
      PARS, Storyboard: space-time representation of THMCR-G processes
      Well supported detailed modelling
    All account for internal THMCR-G processes and their coupling
    All account for external events (including global climatic evolution)
    All account for human intrusion
    All account for evolution of THMCR-G processes with time
      Timeframes may be given by regulation, defined according to specific FEPs (ex: glaciations) or defined according to THMC-G processes (ex: thermal phase)
Conclusions 3/4
    Trends
      Time-space phenomenological representation of FEPs
      Account for the use of safety functions and qualitative uncertainty analyses for derivation of scenarios
      Some probabilistic approaches

## Slide 24
Conclusions 4/4
    Perspectives
    Some national regulations or guides are under revision
      some will include detailed requirements relative to analysis of the repository system
    Some organisations will consolidate their approach for identification, analyses and conceptualisation of FEPs
      New step of data acquisition
      Involvement in international projects
      Taking account of safety functions
      Explore transient phases
        study of coupling of processes and develop their modelling
      Development of probabilistic approaches