## Slide 1
Effects of dimensionality on flow and transport calculations
André Rübel

## Slide 2: Effects of dimensionality on flow and transport calculations
Aim
  Identify the needs for implementing more sophisticated approaches in PA based on a quantitative comparison of different models that feature different complexities of underlying assumptions and process conceptualizations.
  Examine whether the use of more detailed flow and transport codes provide an added value, e.g. by reducing conservatism of the results
  Comparison of results from PA codes with more detailed flow and transport codes which are believed to represent the process adequately

## Slide 3
Clay as a host rock: CEA – IRSN – SCK·CEN

## Slide 4: Clay as host rock: Objectives
3D, 2D and 1D radionuclide transport calculations (129I, 135Cs, 79Se, 245Cm chain)
COMSOL, Cast3m, Goldsim, Melodie , PORFLOW
Study the impact on radionuclide transport calculations of different modelling/numerical aspects including:
  Dimension of modelling (1D, 2D or 3D).
  Disposal geometry (cylindrical gallery section geometry vs. square section).
  Time and space level of refinement (time step and mesh).
  Spatial scheme methods (Finite Element, Mixed Hybrid Finite Element, Finite Volume).

## Slide 5: Clay as host rock: Calculation domain
Cell
Access Drift
Host rock
Bentonite plug
Backfill
Vitrified Waste
Symmetry
Concrete
Calculation area

## Slide 6: Clay as host rock: 3D/2D representation

## Slide 7: Clay as host rock: Results
135Cs (Sorption)
129I (Tracer)
245Cm (chain – 237Np)
79Se (Solubility limit)

## Slide 8: Clay as host rock: Conclusions
No numerical method and time and space discretisation impact for fine problem description.
  Modeller choice (pros and cons of the method).
Small geometry influence.
  Caution with solubility limited release.
  Induced error available.
Dimensionality influence.
  Caution with 1D modelling (solubility limited).
  2D is the best compromise between computation time and accuracy.
  Induced error available.
  3D not always workable.
Deliverable D4.2.4

## Slide 9
Overburden of a repository in salt: GRS

## Slide 10: Geological cross section

## Slide 11: Abstracted cross section
Recharge
Discharge
In/outflow
16 400 m
100 m
100 m
50 m
Dissolution of salt
N
S
vertical exaggeration 10 times

## Slide 12: Radionuclide distribution
I-129
U-234
10 000 a
50 000 a
100 000 a
50 000 a
100 000 a
300 000 a

## Slide 13: Abstraction for the 1D-Modell
Averaging of velocities along two transport pathways

## Slide 14: Radionuclide concentrations pathway 2B
Mean velocity used in 1D model
Maximum velocity used in 1D model

## Slide 15: Conclusions
Different radionuclides are transported on different pathways
  Dependant on transport properties
  Fractions of the radionuclides transported on one or the other of the different pathways differs from nuclide to nuclide
  Multiple 1D paths have to be used
1D model overestimates concentrations due to missing dispersion in second dimension
Averaging of velocities results in large uncertainties
High transport velocities may result in the decay chains being in disequilibria
Deliverable D4.2.1