## Slide 1
WP1.1 – Review of methodologies for the Safety Case
Modelling Strategy
José Luis Cormenzana (Enresa)
Final Workshop Hohenkammer (Germany) 28-30 September 2009

## Slide 2: The importance of modelling
Due to the long time and space scales involved, repository long-term safety can not be proven through experiments
The Safety Assessment requires the development of models to study:
  the evolution of the disposal system
  the release and transport of radionuclides
Results obtained with these models, plus
  natural analogues and
  any other arguments available Model validation/verification
will be used to create de Safety Case
Modelling is fundamental to justify the long term safety of the repository

## Slide 3: Work performed
Eleven organisations provided written contributions presenting their approaches and experiences on “modelling strategy”
The different methodologies/points of view were discussed in a workshop in order to
  identify similarities and differences,
  identify gaps and
  reach a common position, when possible
The analysis of the written contributions plus the discussions of the workshop have been used to create the chapter of the handbook on “modelling strategy”

## Slide 4: Main topics identified
Classification of the models
Model validation/verification
Stochastic/deterministic approaches
Duration of the evaluation/timeframes
Complexity of the Safety Assessment models
Simplification in the Safety Assessment models
QA in model development

## Slide 5: Classification of the models
Although the terms used change, the models used in the Safety Assessment by the different partners can be classified:
  On the basis of their objective:
    Repository evolution
    Transport of radionuclides
  On the basis of the part of the repository involved:
    Detailed models to study the evolution of sub-systems, or specific processes
    Integrated models to perform consequence analysis for selected scenarios
Very detailed process level models usually are not included in the SA, but
  They provide the basic knowledge and data to generate SA models
  They can be used to support the additional arguments included in the Safety Case.
The hierarchy of models presented by NDA is applicable to most organisations
  Finish exception
The top level “system model” is usually for consequence analysis, but
  For some scenarios in salt it is not

## Slide 6: Model validation/verification
Verification: is the process of determining whether a computational model correctly implements the intended conceptual model or mathematical model.
  verification is the easy part
  verification is usually done through comparison with analytical solutions and inter-comparison between different codes
Validation: is the process of showing that the model is a good representation of the real system (proof that it is “valid”)
  validation is usually done comparing model results with experimental observations.
  for HLW repositories the long time periods involved make this “validation” unfeasible.
There is an agreement that strict validation is not possible
  SCK-NIRAS introduces the concept of “model qualification”: verify that the model is consistent with the scientific understanding within the assessment basis and that it adequately represents the considered phenomena and interactions.
  NDA considers that validation is equivalent to “build confidence” in the model, using all the means available.
Validation/qualification of the “phenomenological” process level models for very long term predictions can be a complex task:
  validation of “simplified PA” models can be done by comparison with the phenomenological complex process level models

## Slide 7: Stochastic / deterministic approaches
Deterministic and probabilistic calculations are seen as complementary by most partners.
Deterministic calculations are better for system understanding and communication purposes
Both classes of calculations should be included when making the Safety Case
  Stochastic calculations are specially appropriate to deal with parameter uncertainty
  Stochastic sensitivity analysis provides much information on the key parameters controlling repository behaviour
    More information is obtained than in the deterministic sensitivity analysis

## Slide 8: Duration of the evaluation / timeframes
There is an agreement that numerical calculations can be done for 1 million years
A regulator (GRS-K) establishes a period of proof of 1 million years
ANDRA establishes 1 million years as the period of evaluation
Posiva model repository evolution up to 100,000 years and performs dose calculations over 1 million years
NDA performs risk calculations over 1 million years
Other organisations perform calculations for 1 million years: SCK-NIRAS, Enresa and NRI

## Slide 9: Complexity of the Safety Assessment models
In each iteration of the step by step process to develop a safe repository, data and models should improve compared with the previous one.
Models will be better but not necessarily more complex.
  In fact, a better understanding of the system can allow simplifying the models.
  Example from the Belgian repository in clay.
    Previous models represent the formation above and below repository level
    Calculations showed that transport was diffusion controlled and that relevance of advection was very small.
    For the next safety case the model has been simplified to represent only the formation above repository level.
Previous model
New model
Water flow

## Slide 10: Simplifications in the Safety Assessment models
Simplifications are always necessary when modelling a complex system
  Simplifications must be justified
  Lead to the overestimation of the negative effects on the repository or doses
  Simplifications leading to gross overestimation of the effects should be avoided
As stated by IRSN: An approach that balances simplicity, conservatism and realism is likely to be the best starting point for PA modelling.
  This assertion is valid not only for early iterations of the Safety Case, but even for the last SC
  It can be expected that conservatism should be reduced and realism should increase in successive iterations
Simplifications are even more necessary in the models for probabilistic calculations
SCK uses a set of conservative calculations to show compliance with the limits
  No intention of being more realistic
  Alternative cases with more realistic calculations are done too
Very simplified models (such as analytical solutions) can be included in the Safety Case
  To demonstrate understanding of a complex system
  For communication purposes

## Slide 11: Quality Assurance (QA) in model development
QA and consequent documentation of the models and codes are critical due to the long duration of repository development
  knowledge can get lost when experts leave before finalisation of the project
A well established QA programme is considered fundamental by all the partners
The whole process of model generation must be documented, including
  the decisions taken during the model generation and the reasons behind them
  the simplifications done and their justification
Capability to run old codes must be maintained