## Slide 1
WP1.1 – Review of methodologies for the Safety Case
Criteria for input and data selection
José Luis Cormenzana (Enresa)
Final Workshop Hohenkammer (Germany) 28-30 September 2009

## Slide 2: Data generation and use in the SC
Repository development requires decades to complete
A great amount of data will be generated in:
  waste characterisation
  site characterisation
  supporting scientific studies
Proper generation and handling of these data are critical for the Safety Case
Important topic: the generation/justification of the input data required by the models used in the Safety Case

## Slide 3: Work performed
Ten organisations provided written contributions presenting their approaches and experiences on “data selection” for the Safety Case
The different methodologies/points of view were discussed in a workshop in order to
  identify similarities and differences,
  identify gaps and
  reach a common position, when possible
The analysis of the written contributions plus the discussions of the workshop have been used to create the chapter of the handbook on “data selection”

## Slide 4: Main topics identified
Site characterisation – data generation and processing
Waste characterisation – data generation and processing
The role of Sensitivity Analysis in data selection
Data generation for deterministic calculations
Definition of pdf´s for stochastic calculations
Use of expert elicitation
QA for data generation

## Slide 5: Site characterisation
A huge amount of data will be generated during site characterisation:
  How to treat it?
  Before the start of site characterisation a QA programme must available
Site characterisation is done through the development and progressive updating of a series of interrelated Site Descriptive Models (Geology, Hydrogeology, Hydrochemistry, Geotechnical, Transport properties, Thermal properties and Biosphere) - NDA
  The geology model is the framework on which all the other models are built
  Data will be organised around these models
Site Descriptive Models may change significantly as new site information is available
  In the later stages models will become stable as further information is obtained
  This stability is a potential criterion for deciding completion of the investigations
Safety Assessments performed on the basis of generic geosphere data can be done (GRS-B, ENRESA, NRG, NRI, NDA)
  No detailed characterisation of a given site is needed to perform preliminary SA
  These preliminary SA can provide useful guidance for the site characterisation
Agreement: Site characterisation will generate a great amount of data, and requires a particular strategy

## Slide 6: Waste characterisation
Some participants foresee that many different wastes will be disposed of in the repository (Andra and NDA)
  For them waste characterisation (inventory and waste properties) is a complex topic similar to site characterisation
  Handling the great amount of data generated in the waste characterisation requires a specific strategy
Most participants consider only spent fuel or HLW in their assessments and waste characterisation is not so challenging

## Slide 7: Role of Sensitivity Analysis in input data selection
Sensitivity Analyses from previous Safety Assessments:
  Allow to identify data with high/low relevance for the model
  The effort to determine the value or range of values of a parameter should be proportional to its relevance
  But if the models for the new iteration of the SA are different, the conclusions from previous Sensitivity Analysis could not apply
POSIVA intends to include data from sensitivity analyses or bounding calculations in the Models and Data report
  This information will show the effect of the parameter/data on system evolution and doses
Agreement: Sensitivity Analysis from previous Safety Assessments is useful to identify the most important parameters
  This allows to prioritize the efforts of the input data selection process
  In the first iteration of the Safety Case a review of the assessments done by other organisations for similar wastes and host rock can be used, instead

## Slide 8: Data generation for deterministic calculations
“Best estimate” or “conservative” values are usually selected for calculations
SCK points that in SAFIR 2 when trying to obtain “best estimates” of parameters, the values selected usually were in the conservative side:
  The “true” value was lost
ENRESA, SCK.NIRAS and Andra consider useful to generate both “best estimate” and “conservative” values for the parameters.
  This would reduce the tendency to be conservative when selecting “best estimate” values
  Comparison of the results obtained with “best estimate” and “conservative” values provides an indication of the margin of improvement of the repository if conservativeness can be reduced
In Belgium best estimate values are used for the performance of the barriers and conservative for radiological consequences (FANC).
In one case deterministic calculations are done with the median values (GRS-K)

## Slide 9: Definition of pdf´s for stochastic calculations
The uncertainty in the parameters must be identified explicitly during the process of data selection
  These uncertainties will be basis to define the pdf´s to be used in stochastic calculations.
SCK.NIRAS criteria to generate pdf´s for stochastic parameters are similar to those followed by ENRESA and probably other organisations:
  If the uncertainty (range of values) is higher than a factor 5 a logarithm distribution is used. If it is smaller than 5 a linear distribution is used.
  If is considered convenient to give more weight to a given region of values (around the best estimate, for instance) a triangular distribution with a more probable value equal to the best estimate is used. Otherwise, uniform distributions are used
Task 2.2.A of PAMINA has treated this topic
  The results obtained confirm the approach followed by SCK.NIRAS

## Slide 10: Use of expert elicitation in data selection
Expert judgement vs. expert elicitation
Many decisions must be done when selecting data values:
  Expert judgement is present everywhere
  These decisions and the basis for them should be documented
Expert elicitation is a time consuming process that should be used only when other methods can not be used
  Define and follow clear protocols
  Need to ensure the traceability of the process (FANC)
Formal expert elicitation is not of widespread use for data selection
  Only NDA uses it for all uncertain parameter (when a pdf is needed)
  POSIVA uses it only for very uncertain parameters (solubilities)
  The rest of organisations do not use it

## Slide 11: QA for data generation
The QA programme of the repository must include
  Data generation within the project (experiments, site characterisation,..)
  Data selection for the SC
Key requirements:
  Traceability of the whole process of data generation
  Review of the process and the values obtained by independent experts
  Proper documentation of the process
  Data consistency
Many documents will be generated during the process of data generation.
  A document like the “Models and Data report” prepared by POSIVA will be useful
    It presents enough information about the data used in the Safety Case and how it has been generated + References to more detailed reports where full details can be found
  Similar documents have been prepared by NAGRA (Opalinus) and SKB (SR-CAN), and Andra (Dossier 2005)
Agreement: a comprehensive QA programme is necessary to ensure data quality
  Special emphasis on traceability, external review and proper documentation
  A Report summarising the data used and how it has been generated can be one of the main documents of a SC