## Slide 1
Spatial variability in PA: A review with emphasis on the application of
geostatistical methods (PAMINA 2.2.D)
PAMINA Final Workshop September, 28 - 30 2009, Hohenkammer, Germany
Session III: Modelling strategy
K.-J. Röhlig, E. Plischke (TUC)

## Slide 2: Outline
Motivation / introduction
Methods & their categorisation
The examples reviewed
Use of geospatial methods in PA: What can be observed?
Summary of conclusions

## Slide 3: Motivation / introduction
Last years: considerable evolution concerning uncertainty management / uncertainty analysis (scenarios, models, parameters …)
Less well explored: spatial variability and uncertainty resulting from it
Conceptual problems due to wide variety of qualitatively different information sources (exploration drillings, outcrops, geophysics, knowledge of site genesis, pumping and tracer tests, etc.), i.e. variety of “hard” and "soft" information and knowledge which is typical of geosciences but also causes a certain degree of subjectivity

## Slide 4: Two major themes – two contributions to PAMINA 2.2.D
Upscaling  Work by UPV and UCB (next two presentations)
Addressing uncertainty / lack of knowledge caused by spatial variability  review work by TUC  this presentation
  “Traditional” approach usually results in one "best estimate" image of reality (or, at the most, in a very limited number of "variant" images).
  Rapidly growing capacities and capabilities of electronic computing  multiple maps conceivable
  What do we mean by that?  next slides

## Slide 5: Methods for describing (hydro-)geological settings & their categorisation
Kolterman & Gorelick (1995)
  structure-imitating methods
  process-imitating methods
  descriptive methods
Probabilistics provides powerful tools for imitating structures
  May produce best estimates or multiple maps
  May take advantage of
    spatial co-variance / variogram (“classical” geostatistics),
    objective functions (simulated annealing),
    marked point processes (Boolean models, e.g. fracture networks), and
    transition probabilities (Markov chains)

## Slide 6: Example: Models based on 2-point statistics – spatial co-variance / variogram (“classical” geostatistics)
Options: consider …
  discrete variable (e.g. presence / absence of a facies or hydrogeologic unit) or …
  consider continuous variable (e.g. permeability)
Assumptions:
  Reality is a realisation of a (location-dependent) random function (“regionalised variable”)
  this random function has certain invariance properties, e.g. cdf & covariance are invariant against translations (“stationarity assumption/decision” vs. “stationarity property”)

## Slide 7: Example: Models based on 2-point statistics – spatial co-variance / variogram (“classical” geostatistics)
Steps (1):
  general statistics (univariate, bivariate, populations, trends, ...)
  spatial continuity analysis (experimental, model), e.g.: semivariogram  experimental semivariogram

## Slide 8: Bivariate statistics and distance vector
distance vector
Statistics:
Pair no. 1
Pair no. 2
Pair no. 3
Pair no. 4
Pair no. 5
Pair no. 6
Pair no. 7
and tolerance

## Slide 9: Example: Models based on 2-point statistics – spatial co-variance / variogram (“classical” geostatistics)
Steps (2)
  Estimation ( smoothing), i.e. Kriging, indicator kriging and / or
  Simulation (multiple maps, attempt to reproduce heterogeneity)
Properties:
  Account for „hard“ data
  Account for spatial dependencies („points close to each other  similar data“ – role of the semivariogram)

## Slide 10
Example:
Vertical
cross section
through
Gorleben channel
? ? ?
First:
Let‘s drill ...
Saltdome

## Slide 11
First:
Let‘s drill ...
Saltdome
Example:
Vertical
cross section
through
Gorleben channel

## Slide 12
BUT:
What is in between?
?
?
?
?
?
Saltdome
Interpolation: 2 hydrogeological units („clay“, „non-clay“)
Image of low-permeable clay layers by kriging
Non-Clay
Clay
Example:
Vertical
cross section
through
Gorleben channel

## Slide 13
BUT:
How to deal with
Variation of „clay“ shape using geostatistical simulation ...
UNCERTAINTIES?
Non-Clay
Clay
Example:
Vertical
cross section
through
Gorleben channel

## Slide 14
Non-Clay
Clay
BUT:
How to deal with
Variation of „clay“ shape using geostatistical simulation ...
UNCERTAINTIES?
Example:
Vertical
cross section
through
Gorleben channel

## Slide 15: Frequently used: stochastic fracture models
Entities which can be considered:
  fracture location
  fracture size
  fracture orientation (e.g. strike, dip)
  fracture intensity
  fracture termination mode
  fracture aperture
Possible tool: Boolean methods (“throwing” objects with sampled properties into space)
Fig. from Srivastava, 2005

## Slide 16: Review: Application of spatial statistics in PA
Site / system?
Scale
Target of study (e.g. enhance understanding, perform probabilisitic PA etc.)
Method(s) applied
Peculiarities

## Slide 17
Reference | Location | Target | Remarks
(Porter, et al., 1997), (Röhlig, 1998)- (Röhlig, et al., 2005) | Gorleben (Salt): – sedimentary overburden | Modelling of heterogeneities Handling of incomplete geospatial knowledge | Geostatistics 3D, modelling 2D vertically, scale 104 x 102 m2, stepwise integration of different information types, probabilistic for fresh water calculations, iterative approach to density flow
(LaVenue, et al., 1992), (LaVenue, et al., 1995), (Capilla, et al., 1998), (Beauheim, et al., 2007) | WIPP (Salt): overlying beds | Modelling of heterogeneities Handling of incomplete geospatial knowledge Derivation of local sensitivities regarding ground water travel times location of new wells | 2D horizontally, scale 104 x 104 m2, probabilistic in licensing procedure (US DOE, 1996), (US DOE, 2004), later works not for compliance, but for supporting geological understanding in the safety case, calibration with ground water heads
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
Reference | Location | Target | Remarks
(Jaquet, et al., 1998) | Wellenberg: claystone | Handling of incomplete geospatial knowledge | 3D, scale 103 x 103 x 103 m3, “probabilistic“ (12 realisations)
(Deraisme, et al., 2004), (Jaquet, et al., 2003), (Jaquet, et al., 2006) | Äspö: crystalline | Modelling of heterogeneities | 3D, scale 105 x 104 x 103 m3, density dependent flow, used for licensing in (Auqué, et al., 2006), (SKB, 2006)
(Jaquet, et al., 1999) | Site du Gard: clay and overlying cretaceous deposits | Modelling of heterogeneities | 3D, scale 104 x 104 x 103 m3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19
Reference | Location | Target | Remarks
(Xu, et al., 2000), (Wörmann, et al., 2003) | Äspö: crystalline | Modelling of heterogeneities | 1D calculation of migration, scale 10-3…10-2 m
(Huysmans, et al., 2005) | Mol: Boom Clay (ductile) | Modelling of heterogeneities in the host rock including fracturing of the EDZ | Simplified 3D-model (symmetry assumption) for calculation of migration, scale 101 x 101 x 102 m3
(Srivastava, 2007) | Hypothetical Canadian crystalline site | Modelling of large scale fractures (based on statistics of the Canadian Shield, uncertainty considerations planned for several realisations) | 3D, scale 84 km2 x 1,5 km
(Park, et al., 2004), (Park, et al., 2005) | Whiteshell / Lac du Bonnet: crystalline | Derivation of spatially varying effective properties for fractured material Prediction of tracer test results | Scale 50 m x 50 m x 50 m, calibration of conductivities, porosity, dilution by categorical Markov-realisations
(McKenna, 2001) | MIU, Japan: crystalline | Modelling of heterogeneities | 3D, scale 103 x 103 x 103 m3
(Iooss, 2008) | Moscow: sands and clays | Modelling of heterogeneities Sensitivity analysis | Scale 250 m × 350 m, 3 vertical layers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Use of geospatial methods in PA and SC (1)
Stepwise SC evolution – feedback to R&D
  Borehole locations – WIPP
  Glaciation studies (replace questionable models – SKB)
Complex vs. “simplistic” models
  Justification (ONDRAF.NIRAS)
  Parameter derivation (SKI)
Most work only indirectly connected to PA; rather support geological understanding for use in a safety case. Exceptions:
  WIPP
  Established: fracture networks (OPG, SKB)

## Slide 21: Use of geospatial methods in PA and SC (2)
Recent years: more emphasis on safety functions
  All studies reviewed: “delay or attenuation of radionuclide migration in the host rock or the overburden”
  None: “containment” or “(mechanical/ chemical / thermodynamical /hydraulical / geological) stability” (maybe glaciation study can be connected to “hydraulic stability”)
  Field for improvement? (e.g. by using parameters varying in space in geomechanic calculations  “Mechanical stability”)
Probabilistic SA
  Simulation (both variogram-based and Boolean): potential of representing uncertainties caused by spatial variability in an integrated probabilistic safety assessment model
  WIPP! (regulation being a strong driver)

## Slide 22: Summary of conclusions
SA became increasingly focussed on safety functions
Hydrogeological modelling as means for consequence calculations: decreasing weight in many concepts
Nevertheless: safety cases …
  should discuss spatial variability with regard to its potential of influencing or jeopardizing the safety functions claimed,
  investigate, where necessary, its impact, and
  either justify its omission in assessments or explicitly account for it.
Review demonstrates that the means of doing so are available (not necessarily restricted to the traditional application area of hydrogeological and migration modelling, but might, dependent on the safety concept, well be useful for other areas)
Notes: <number>
<footer>
<header>
<date/time>