## Slide 1
Near-field processes in salt
André Rübel

## Slide 2: Collaborators…
D. Buhmann (GRS)
J. Grupa (NRG)
J. Hart (NRG)
R.-P. Hirsekorn (GRS)
A. Ionescu (GRS)
C. Lerch (DBE)
A. Rübel (GRS)
A. Schneider (GRS)
T. Schröder (NRG)

## Slide 3: Process representation in PA models
Aim
  Examine whether certain complex processes which are relevant for the repository system are adequately represented by high abstracted models in the PA codes or if a more detailed approach is needed
  Comparison of results from PA codes with state-of-the-art process-level codes which are believed to represent the process adequately
Process model  PA model

## Slide 4: Convergence of rock salt

## Slide 5: Convergence of rock salt

## Slide 6: Convergence of rock salt
14 different test cases
Process model
  FLAC 3D (DBE)
PA models
  REPOS (NRG)
    Calibration on external data
  LOPOS (GRS)
    Calibration on first test case
Good agreement of PA models with process model

## Slide 7: Brine intrusion into a backfilled drift
Shaft 800m
Drift

## Slide 8: Brine intrusion into a backfilled drift

## Slide 9: Brine intrusion into a backfilled drift
Process model
  HYDRUS 2D (GRS)
  Two-phase flow (van Genuchten model)
PA models
  REPOS (NRG)
    Darcy-flow / adapted permeability
  LOPOS (GRS)
    Darcy-flow / adapted pressure
    Different discretisation cases
Satisfactory agreement of PA models with process model

## Slide 10: Convective flow and convective flow driven radionuclide transport

## Slide 11: Convective flow

## Slide 12: Convective flow
Process models
  PORFLOW (NRG)
  d3f/r3t (GRS)
PA models
  Semi-analytical model (NRG)
  REPOS (GRS)
Good agreement of semi-analytical model and process model
Inadequate representation of convective flow/transport in the REPOS models

## Slide 13: Conclusions
Convergence of rock salt
  Good agreement between PA and process level codes
  Currently no further action required
Brine intrusion into a backfilled drift
  Good agreement between PA and process level codes
  Further comparison might be useful when better process representation will be available
Convective flow
  Inadequate representation by PA model
  Good agreement of semi-analytical model by NRG
  Implementation of semi-analytical model in the PA code has to be considered in the future
Results are presented in deliverable D4.1.1