## Slide 1
PAMINA Final Workshop – Hohenkammer– Sept 28th- 30th 2009
Review of upscaling methods and application to granites
Javier Rodrigo-Ilarri
Hydraulic and Environmental Engineering Department
Universidad Politécnica de Valencia (Spain)
Notes: <number>

## Slide 2
<number>
What is upscaling?

## Slide 3
<number>
Task 2.2.D - Spatial Variability
&
WP 4.2 - PA Approaches Based on Different Geometry Complexity of Modelling
To research the issue of “upscaling”, and its impact on the uncertainties of radionuclide transport in the geosphere
To undertake a series of exercises to evaluate the advantages and disadvantages of different methods in the treatment of upscaling in the flow and transport of radioactive species through a host rock
Our duties following PAMINA Project objectives were:
Our work has been focused on:
Review the available methods to treat the issue of upscaling  “State of the Art on Upscaling”
Perform a series of exercises to evaluate the impact of upscaling on the uncertainty in performance assessments for repositories in granite rocks.
Notes: <number>

## Slide 4
<number>
Task 2.2.D Spatial Variability
Document: “State of the Art on Upscaling Techniques”
  Flow parameters
  Transport parameters
Milestone 2.2.D.3
Plan for PA exercises to evaluate upscaling
Milestone 2.2.D.2
Deliverable 2.2.D.1
Evaluation and Testing of Approaches to treat Spatial Variability in PA
Document: “Review of Spatial Variability in PA”
Milestone 2.2.D.1
Notes: <number>

## Slide 5
<number>
Task 2.2.D Spatial Variability
Acknowledgment to the authors:
TUC – Technical University of Clausthal
Elmar Plischke
Klaus-Jürgen Röhlig
CEA –Commissariat à l’Énergie Atomique
Bertrand Iooss
UPV – Technical University of Valencia
J.Jaime Gómez-Hernández
Javier Rodrigo-Ilarri
Notes: <number>

## Slide 6
<number>
Deliverable 2.2.D.1 - Evaluation and Testing of Approaches
to treat Spatial Variability in PA
217 pages
Available on PAMINA web site for downloading
INDEX:
1.- State of the Art on upscaling techniques
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
3.- Review of spatial variability in Performance Assessments
4.- Plan for PA exercises to test techniques for upscaling
Notes: <number>

## Slide 7
<number>
Deliverable 2.2.D.1 - Evaluation and Testing of Approaches
to treat Spatial Variability in PA
217 pages
Available on PAMINA web site for downloading
INDEX:
1.- State of the Art on upscaling techniques
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
3.- Review of spatial variability in Performance Assessments
4.- Plan for PA exercises to test techniques for upscaling
Notes: <number>

## Slide 8
<number>
1.- State of the Art on upscaling techniques
Notes: <number>

## Slide 9
<number>
1.- State of the Art on upscaling techniques
Notes: <number>

## Slide 10
<number>
Deliverable 2.2.D.1 - Evaluation and Testing of Approaches
to treat Spatial Variability in PA
217 pages
Available on PAMINA web site for downloading
INDEX:
1.- State of the Art on upscaling techniques
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
3.- Review of spatial variability in Performance Assessments
4.- Plan for PA exercises to test techniques for upscaling
Notes: <number>

## Slide 11
<number>
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
Notes: <number>

## Slide 12
<number>
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
Notes: <number>

## Slide 13
<number>
Deliverable 2.2.D.1 - Evaluation and Testing of Approaches
to treat Spatial Variability in PA
217 pages
Available on PAMINA web site for downloading
INDEX:
1.- State of the Art on upscaling techniques
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
3.- Review of spatial variability in Performance Assessments
4.- Plan for PA exercises to test techniques for upscaling
Notes: <number>

## Slide 14
<number>
3.- Review of spatial variability in Performance Assessments
Notes: <number>

## Slide 15
<number>
Deliverable 2.2.D.1 - Evaluation and Testing of Approaches
to treat Spatial Variability in PA
217 pages
Available on PAMINA web site for downloading
INDEX:
1.- State of the Art on upscaling techniques
2.- Treatment of spatially dependent input variables in sensitivity analysis of model output methods
3.- Review of spatial variability in Performance Assessments
4.- Plan for PA exercises to test techniques for upscaling
Notes: <number>

## Slide 16
<number>
4.- Plan for PA exercises to test techniques for upscaling
PART 1.- General treatment of upscaling on the PA Exercises
PART 2.- Upscaling of flow parameters
PART 3.- Upscaling of transport parameters
END of work on WP2.2.D
Application to granites on WP4.2
Notes: <number>

## Slide 17
<number>
PA codes model the transport of radionuclides in the geosphere often using a fairly simple 1D approach.
In this WP transport has been evaluated using a more complex modelling approach
WP 4.2 PA Approaches Based on Different Geometry Complexity of Modelling
Granite Simulations

## Slide 18
<number>
WP 4.2 Granite Simulations
Available data provided by ENRESA
The benchmark case specification, was prepared jointly with ENRESA (Milestone 4.2.2 and Milestone 4.2.5)
A series of exercises of radionuclide transport in the granite host rock have been performed.

## Slide 19
<number>
WP 4.2 Granite Simulations
SISIM: 3 families of stochastic fractures
4 deterministic fractures
SGSIM: Matrix
440 * 640 blocks

## Slide 20
<number>
WP 4.2 Granite Simulations
Geometric model

## Slide 21
<number>

## Slide 22
<number>
WP4.2 Granite Simulations - FLOW UPSCALING
A Laplacian approach with skin (Gómez-Hernández, 1991) is used to upscale the 440x640 fine scale conductivity field to a 44x64 coarse scale
The cell size of the coarse field is 100x100 m.
A full conductivity tensor is obtained with this method
The fur deterministic fractures play an important role in the K field even in a coarse scale
When upscaling flow the objective is to preserve the total flow crossing the sides of the coarse model blocks
Model Parameters
Laplacian approach with skin
44 * 64 blocks
Porosity=0.0001
Deterministic Fracture Logk=-8.6
Stochastic Fracture LogK=-9.6
Matrix LogK=-11.
No recharge.
Conductivity Tensor Components

## Slide 23
<number>
WP4.2 Granite Simulations - FLOW UPSCALING
Different upscaling techniques are compared:
  Geometric averaging of the permeability values within the block
  Laplacian with skin, considering diagonal permeability tensor
  Laplacian with skin, considering full permeability tensor
Coarse scale (x-axis) vs. fine scale (y-axis) fluxes through block interfaces for the different upscaling approaches
Geometric
Diagonal Tensor
Full Tensor

## Slide 24
<number>
WP 4.2 Granite Simulations - TRANSPORT UPSCALING
The first simulation of transport at the coarse scale was aimed to analyze whether purely advective transport at the fine scale could be reproduced by purely advective transport at the coarse scale after performing flow upscaling with a full tensor.
The reproduction of the fine scale results is acceptable although we have observed:
  an overestimation of the early arrival times and
  an underestimation of the late arrival times
The discrepancy between the two curves is due to the unresolved within block dispersion that is not transferred to the coarse model
To improve the results, Fernàndez-Garcia et al. (2007) propose to model a mass transfer process in each block which mimics the dispersion/retardation induced in the fine scale by the heterogeneity within the block.
Using this approach, the results improve although there is still some overestimation of the early arrival times

## Slide 25
<number>
WP 4.2 Granite Simulations - TRANSPORT UPSCALING
No upscaling
Advective transport
Only Flow upscaling
Advective transport
Fine grid
Coarse scale simulation
Flow and transport upscaling using mass transfer with a double-rate model
Advective transport

## Slide 26
<number>
WP 4.2 Granite Simulations - TRANSPORT UPSCALING
Fine scale
Coarse scale
Mass transfer
Fine scale
Coarse scale
Mass transfer
Cumulative breakthrough curve at the north boundary
Linear and log scales for the time axis and for the normalized mass.
Comparison between the results on the fine scale, on the coarse scale without transport upscaling and on the coarse scale with transport upscaling using the mass transfer approach
Log (Time)
Time
Mass
Log (Normalized Mass)

## Slide 27
<number>
WP 4.2 Granite Simulations - TRANSPORT UPSCALING
Fine scale
Coarse scale
Mass transfer
Fine scale
Coarse scale
Mass transfer
Cumulative breakthrough curve at the north boundary
Linear and log scales for the time axis and for the normalized mass.
Comparison between the results on the fine scale, on the coarse scale without transport upscaling and on the coarse scale with transport upscaling using the mass transfer approach
Log (Time)
Time
Mass
Log (Normalized Mass)
Overestimation of early arrival times

## Slide 28
<number>
Some Conclusions
The results of the transport simulations on the coarse scale considering the two orders of magnitude reduction in the numerical model size are remarkable
It has been demonstrated the importance of properly choosing an upscaling method to simulate flow and transport at coarser scales
In the case of flow in fractured media it is very important to account for the tensorial nature of hydraulic conductivity
In the case of transport it is important to use upcaling techniques that can preserve the residence time of the solutes within the block when moving from the fine scale to the coarse scale.
Scenarios considering matrix diffusion and sorption processes have also been developed. Results will be available on the Final Report.

## Slide 29
<number>
PAMINA Conclusions
Our work on WP 2.2 & WP 4.2 are related to each other
Task 2.2.D (jointly with TUC & CEA)
  M 2.2.D.1 - Review of Spatial Variability in PA
  M 2.2.D.2 - The State of the Art on upscaling techniques
  M 2.2.D.3 - Plan for PA exercises to evaluate upscaling
  D 2.2.D.1 - Evaluation and Testing of Approaches to treat Spatial Variability in PA
WP 4.2 (jointly with ENRESA)
  M 4.2.2 and M.4.2.5 – Benchmark of the granite case
  Different Progress Reports have been delivered
  Final Report will be ready in a matter of days

## Slide 30
PAMINA Final Workshop – Hohenkammer– Sept 28th- 30th 2009
Review of upscaling methods and application to granites
Javier Rodrigo-Ilarri
Hydraulic and Environmental Engineering Department
Universidad Politécnica de Valencia (Spain)
Notes: <number>