## Slide 1
Uncertainties Associated with Modelling the Consequences of Gas
Simon Norris, Lucy Bailey, Helen Clark and Matthew Wellstead
PAMINA Workshop
28th-30th September 09
Notes: Study relates to uncertainties in modelling gas from GDF in generic environments in UK
Only considering ILW in this study

## Slide 2: Structure
Introduction
Gas Generation
  Scenarios
  Calculations
Gas Migration
  Variant geologies
  1-D and 2-D models
Conclusions
Notes: Presentation divided into 2 parts

## Slide 3: Introduction
  The aims:
    Understand how calculated gas generation and migration vary with modification to the scenario parameters
    Address treatment of uncertainty through sensitivity studies
  Scoping of uncertainty in the rate of gas generation
    Reference case based on previous study
    Four variant scenarios
  Gas migration calculations
    Based on reference case
    Variant calculations based on three geologies
Notes: Gain an understanding of how gas generation/migration model results vary by changing the parameters
Use sensitivity studies to address our treatment of uncertainties
Our gas generation reference case was used as the basis to develop our gas migrations models

## Slide 4: Scenarios for Gas Generation
Reference case scenario and four variants:
  Varying temperature case
  Exclusion of carbonation case
  Small organic molecules case (not discussed in this presentation)
  Operational case
Notes: Varying temp case – we assumed a higher temperature just before and after closure.
Exclusion of carbonation – allows CO2 to form (not captured by our backfill)
Small Organic – UK specific stream
Operations – parameters chosen to give more realistic values for operations prior to closure.
Key features from the results for our gas generation model are shown on in the following plot our reference case

## Slide 5: Reference Case Scenario
Bulk gases
Active gases
Notes: Gas generation commences from time of emplacement
Increases as more waste is added.
Aerobic conditions. From closure GDF starts to resaturate giving acute corrosion of active metals (releasing H2, 14CO2, 3HH, Rn222)
After 5 years anaerobic conditions established. Generation rates reduced.
CO2 is captured by the backfill.
Ingrowth from U238.
Formation of methane when sulphate/nitrate consumed.
14CH4 decreases due to magnox+small organics consumption(+decay)
Before emplacement H2 formed from degradation of polymers. U-metal + Steels give off 3HH and 14CH4 (also from radiolysis of small organic molecules)
Resaturation – Al+Magnox give of H2 and 3HH (and from tritiated H2O). Magnox gives off 14CH4.
Anaerobic – U + steels generate H2 and 3HH. Zircaloy +mild steel acute corrosion
H2 and 3HH rates decrease due to consumption of magnox waste (and hence H2O)
14CH4 decreases due to magnox+small organics consumption(+decay)

## Slide 6: Scenario Differences
Varying temperature case
  Increased corrosion rates
Exclusion of carbonation case
  CO2 formation
  CH4 formation after O2, sulphate and nitrate exhausted
Operation Case
  Organic degradation starts after packaging
  Reactive metals corrode prior to closure
  Radiolysis of H2O
Notes: Temp: more rapid corrosion, but also quicker consumption (U and Magnox corrode before the anaerobic phase.)
Exclusion: CO2 formed from organic degradation. Increase in 14CO2. CO2 available to form CH4 from H2 when no O2, nitrate/sulphate
Op:
Diffusion of tritium from the steels in the waste is the dominant process for releasing this active gas.
After the reactive metals are all corroded, corrosion of steel becomes an important source of 14C in methane. In the case of the SILW/LLW vaults, 14C in methane is also released as a result of the degradation of graphite.
The rate of production of 222Rn within the wasteform can be calculated readily from the activity of 226Ra present. However, the radiological consequences arising from 222Rn generated in the repository are insignificant because of the short half-life of this radionuclide. The dose from 222Rn arises from radon that is ‘stripped’ from the Quaternary sediments rather than from radon that originates in the repository.

## Slide 7: Gas Migration Calculations
Aim
  Investigate model sensitivity to input parameters
Models
  1-D model of a generic fractured crystalline host rock
  1-D model of a generic argillaceous host rock
  2-D model based on an historic dataset from a UK geology
Natural fracturing of sandstone
Notes: 1-D model outputs are pressure in the GDF over time and time of breakthrough.
Will discuss the results from 1-D models in the summary
At present we don’t have a site in the UK
Gas migration was studies using simple 1 dimensional TOUGH2 calculations.
These are simplistic calculations undertaken without an identified or characterised potential site.
In practice the occurrence of viscous fingering and the presence of 3D variability in the rock (including the presence of fractures) could modify the results obtained, in particular reducing the break through times.
Three variant 2D calculations designed to scope the effect of fingering were carried out. Only some of the variants led to the breakthrough of a free gas phase.

## Slide 8: Two-Dimensional Model of Gas Migration from a Repository
8,150 years post closure
Gas saturation, 15 years post-closure
33 years post closure
Notes: X-sec thorough the GDF and surrounding geology
enclosures represent geological untis and lines represent fractures each assigned appropriate properties.
Vertical scale is depth from surface. Horizontal scale is distance
GDF, expected evolution of free gas phase. Pressure build up in GDF, gas release.
Over time free gas phase flows along fractures specific to the site geology
Geology and structure important. Can see gas collecting in pocket.
Over 1000s of years gas dissolved into groundwater.
By about 1000 years after closure the free gas pathway would collapse.
After this, gas would migrate in solution in the groundwater.
It is suggested that most of the dissolved gas would flow across the left-hand boundary of the model. The left-hand boundary is at the coast, and so the flows across this surface are assumed to be discharging to sea.
The flow of dissolved gas across the top boundary of the model could be substantially less than the gas generation rate.
Any dissolved gas that flows across the top surface of the model could be released over most of the area between the GDF and the coast.

## Slide 9: Two-Dimensional Model of Gas Migration from a Repository
Gas saturation (in this variant, the gas solubility is reduced to 1% of its true volume) -25 years post-closure.
250 years post closure
9,400 years post closure
Notes: Mimicked less interaction with water by decreases solubility
Gas migration along fractures and features to surface is clear to see
Flows into pocket where pressure builds until gas moves along to the surface
Breakthrough at 25 yrs post closure
Initially localised and then spreads out below the surface before breaking up.
The free gas pathway could be focussed (e.g. by the presence of a fault) and so could flow across the top surface of the model through an area that is much less than that of the repository. This is shown in the figures on this slide.
At the time of breakthrough the free gas flow could be larger than the generation rate.
Free gas might contact only part of the groundwater within the rock volume represented by a grid block. (This is known as viscous fingering).
Depending on the extent to which this happens a free gas phase could break through at the top boundary.
If a free gas pathway were to form, it would spread out below the top surface of the model.

## Slide 10: Summary of Gas Migration Calculations
Our 1-D calculations showed
  In the fractured crystalline host rock model breakthrough occurs at approximately 7,500 years post-closure.
  In the argillaceous host rock model there is no breakthrough.
  Uncertainty about the mechanism of gas migration
Our 2-D calculations showed
  No free gas released if it “sees” all available groundwater
  Minimal contact with water gives rise to free gas pathway to surface
  Uncertainty with how much water the gas “sees”

## Slide 11: Summary
Uncertainties associated with modelling the consequences of gas have been scoped
  Development of variant cases of gas generation and migration
Some uncertainties still require further study
  Mechanism of gas migration in low-permeability argillaceous materials
  Interaction with water
Details of gas migration are very site-specific.
  Rock heterogeneities
  Geological disposal facility design
Notes: can’t perform detailed gas calculations as they are very site specific.
After identifying a site we will be able to develop and refine more detailed models based on available data.

## Slide 12: Acknowledgements
This presentation relates to work reported in:
PAMINA Task 2.2B Model Uncertainty Topic 2 Uncertainties Associated with Modelling the Consequences of Gas, Simon Norris, NDA March 2008.
This report draws on the information presented in:
Update of the GPA (03 Assessment of the consequences of Gas, Serco report SA/ENV-0948 Issue 1, Andrew Hoch, Mike Thorne, Ben Swift and Fiona Bate, March 2007)
On Gas Migration Beneath a Dipping Low Permeability Horizon with Leakage, Andrew Woods and Adrian Farcas, BP Institute for Multiphase flow, University of Cambridge, November 2007.
Notes: Acknowledge Simon Norris
Thank you
Any questions