## Slide 1
Session IV: Safety and Performance Indicators
A Review
Jens Wolf (GRS)
Notes: <number>

## Slide 2: Outline
Background / Retrospective / Synthesis of research
  Development of the term safety indicator
  Distinction between safety indicators and performance indicators
The work in PAMINA WP3.4 (PAMINA WP 1.1)
  Common views
  Applied indicators
  Results (second presentation)
Role of safety and performance indicators in the safety case
Conclusions
<number>

## Slide 3: Safety Indicators
<number>
The long-term safety of a repository system cannot be reduced to one single numerical measure (dose or risk)
IAEA TECDOC 767 (1994)
IAEA CRP on Safety Indicators (1999 - 2003) Methodology: →TECDOC 1372, Criteria: →TECDOC 1464 (2005)
SPIN (2000 - 2002) (test case: granite) → EUR 19965 EN
IAEA Safety Standard Series WS-R-4, §2.18, §3.35 (2006)
NEA / OECD Post-Closure Safety Case for Geological Repositories (2004)
PAMINA WP1.1, WP 3.4 (test cases: clay, salt and granite)
International Consensus (e.g. NEA / OECD + IAEA 1991):

## Slide 4: Safety and Performance Indicators
<number>
TECDOC 1372
EUR 19965 EN
In both documents a distinction is made between safety indicators and performance indicators
PAMINA WP1.1: Collection of views and the understanding of safety indicators and performance indicators of the participating organisations
→ most countries use SPIN / IAEA definitions as starting point
→ but today there is a wide variety of individual terminology/views
Harmonisation of definitions within WP3.4
D-N°:3.4.2

## Slide 5: Safety Indicators
<number>
Primary Safety Indicator (PSI):
Effective Dose Rate [Sv/a] (Risk [1/a])
Complementary Safety Indicator (CSI):
CRP (3 CSI were initially selected , 2 CSI are recommended):
Radionuclide concentration outside the near field [Sv/m3]
Radionuclide fluxes outside the near field [Sv/a]
SPIN (6 CSI were initially selected , 2 CSI are recommended):
Radiotoxicity concentration in biosphere water [Sv/m3]
Radiotoxicity flux from the geosphere [Sv/a]
PAMINA WP3.4 (one new indicator):
Power density in ground water [MeV/(s∙m3)]
Regulator
Regulator or Implementer?

## Slide 6: Safety Indicators in different time frames
<number>
Effective Dose Rate
Radiotoxicity concentration in biosphere water
Radiotoxicity flux from the geosphere
Power density in ground water
Time
early
medium
late
No cut-off criteria: SI should be applied to all time frames, but there are preferences

## Slide 7: Reference Values
<number>
Effective Dose Rate [Sv/a] or Risk [1/a]
Regulatory constraint, legal limit (10-4 Sv/a, risk of 10-6 a-1)
Radiotoxicity concentration in biosphere water [Sv/m3]
Natural background values
Radiotoxicity flux from the geosphere [Sv/a]
Natural background values
Power density in ground water [MeV/(s∙m3)]
Natural background values
Scale
global
regional (to local)
(regional) to local
regional (to local)

## Slide 8: Reference Values used in WP 3.4
<number>
 | ENRESA | SCK∙CEN | NRG | NRI | GRS
Effective dose rate (mSv/a) | 0.1-0.3 | 0.3 | 0.3 | 0.25 | 0.1
Radiotoxicity concentration in biosphere water (Sv/m3) | 2∙10-5 | 2∙10-5 | 2∙10-5 | 4∙10-6 | 2∙10-6
Radiotoxicity flux from the geosphere (Sv/a) | 60 | 10 | 60 | 8 | 0.1
Power density in biosphere water (MeV/s·m3) | 80 | - | 80 | - | 25

## Slide 9: Performance Indicators
<number>
SPIN (14 PI were selected and tested):
… the selection of a PI will depend mainly on the specific problem investigated.
No general recommendations
PAMINA WP3.4:
Indicators based on inventories or concentrations
Indicators based on fluxes
Indicators based on integrated fluxes
Indicators based on safety functions
Indicators based on transport times
Indicators based on characteristics of the salt host formation (e.g. “time to plug closure” [salt])

## Slide 10: …. in the Safety Case
<number>
Performance Indicators
Safety Indicators (PSI + CSI)
Performance Indicators
Performance Indicators
Performance Indicators
From NEA / OECD (2004) : Post-Closure Safety Case for Geological Repositories
managing uncertainties
optimising concepts
increasing transparency

## Slide 11: Conclusions
<number>
Common view: Primary safety indicator is the effective dose / risk, but complementary safety indicator are necessary arguments for the safety case
Tendency: PSI → Regulator (limit or constraint), CSI → Implementer Reference values for CSI specific for DGR, the choice of CSI is dependent on the context of each national programme
The development of the national programmes has led to different definitions and approaches
The definition in WP3.4 is closely related to the SPIN project Recommendation: Safety indicator (overall safety, safety-relevant reference value) A more flexible definition for performance indicators allow the coverage of different concepts → Implementer
The derivation of reference values can become complicated
The discussion is going on … → LTSC, IGSC MeSA

## Slide 12: Can long-term safety be evaluated?
<number>
NEA/IAEA/CEC Symposium on Safety Assessment of Radioactive Waste Repositories, Paris 1990
Starting point of the discussion on safety indicators
1991: The International Radioactive Waste Management Advisory Commitee (INWAC) established the subgroup
INWAC Subgroup on Principles and Criteria for Radioactive Waste Disposal

## Slide 13: IAEA TECDOC-767
<number>
Safety indicators in different time frames for the safety assessment of underground radioactive waste repositories
Summary
1. The assessed long term consequences of disposal systems in terms of risk and dose can
only be considered as indicators of safety.
2. The long term safety case can be made most effectively by the combined use of several
safety indicators, such as risk, dose, environmental concentration, biospheric flux, flux through barriers and time recognising, however, that risk and dose remain the most
fundamental of the indicators of safety.
3. Indicators become particularly valuable when they are supported by observations from
natural analogues.

## Slide 14: Definitions IAEA TECDOC 1372
<number>
A distinction is also drawn between a performance indicator and a safety indicator.
A performance indicator provides measures of performance to support the development of system understanding and to assess the quality, reliability or effectiveness of a disposal system as a whole or of particular aspects or components of a disposal system
A safety indicator, which may be regarded as a special type of performance indicators, is used to assess calculated performance in terms of overall safety.
Safety indicators for the safety assessment of radioactive waste disposal

## Slide 15: Definitions SPIN report
<number>
A safety indicator must
provide a measure of the safety of the whole system
allow a comparison with safety-relevant reference value
take into account the contributions of all radionuclides
be calculable using performance assessment models
A performance indicator must
provide a measure of the safety of the whole system or a subsystem
allow a comparison between different options or with technical criteria
take into account the contributions of all radionuclides or a single radionuclide
be calculable using performance assessment models
Performance indicators can be derived through a systematic approach using safety functions. → second presentation

## Slide 16: Definitions PAMINA WP 3.4
<number>
Strict definition for safety indicator, broad definition for performance indicator
A safety indicator is a quantity, calculable by means of suitable models, that provides a measure for the total system performance with respect to a specific safety aspect, in comparison with a reference value quantifying a global or local level that can be proven, or is at least commonly considered, to be safe.
A performance indicator is a quantity, calculable by means of appropriate models, that provides a measure for the performance of a system component, several components or the whole system.

## Slide 17: Radiotoxicity concentration in biosphere water
<number>
- represents the radiotoxicity of the radionuclides in 1 m3 of biosphere water. - calculated as
- the ingestion dose coefficient Dn represents the dose caused by ingestion of radionuclide n (Sv per ingested Bq, ICRP (1996))
- the effects of daughters produced in vivo are accounted for in the ingestion dose coefficients

## Slide 18: Radiotoxicity flux from the geosphere
<number>
The radiotoxicity flux from the geosphere is calculated as
sn is the activity flux [Bq/a] of radionuclide n from the geosphere to a water body, which represents the interface to the biosphere - eliminates the uncertainty from the dilution in this water body, but has only a weak relation to human health
reference value often derived from concentrations!
!!

## Slide 19: Power density in groundwater
<number>
The power density in groundwater is calculated as
- cn is the activity concentration [Bq/m3] of radionuclide n in groundwater
En the decay energy
yields a power density p [MeV/(s∙m3)]
criterion for the impact of radionuclides on biota in general
[originally proposed by GRS for the new German safety requirements]

## Slide 20: Derivation of Reference Values
<number>
Nuclide | Ingestion dose coefficient [Sv/Bq] | Activity concentration* [Bq/m3] | Radiotoxicity concentration [Sv/m3]
U-238 | 4.50∙10-8 | 5.0 | 2.25∙10-7
U-234 | 4.90∙10-8 | 6.0 | 2.94∙10-7
Ra-226 | 2.80∙10-7 | 5.0 | 1.40∙10-6
Rn-222 | 3.50∙10-10 | 5 900 | 2.07∙10-6
Pb-210 | 6.90∙10-7 | 1.5 | 1.04∙10-6
Po-210 | 1.20∙10-6 | 0.5 | 6.00∙10-7
Th-232 | 2.30∙10-7 | 0.1 | 2.30∙10-8
Ra-228 | 6.90∙10-7 | 3.0 | 2.07∙10-6
Th-228 | 7.20∙10-8 | 0.2 | 1.44∙10-8
U-235 | 4.70∙10-8 | 0.3 | 1.41∙10-8
Total |  |  | 7.74∙10-6
Proposed safety factor for reference values: 0.3
→ Reference value: 2∙10-6 Sv/m3
Example: Radiotoxicity concentration in biosphere water (Sv/m3)
* published by the Federal Ministry for the Environment, Nature Conservation and Nuclear Safety (2003)

## Slide 21: Post-Closure Safety Case for Geological Repositories
<number>
NEA / OECD (2004)