## Slide 1
Session IV: Safety and performance indicators
Case studies for salt, clay and granite as host rock
T.J.Schröder, NRG

## Slide 2: WP3.4: Repository systems analysed
Six repository systems in three different types of host rocks:
normal evolution
abandonment
scenario
normal evolution
normal
evolution
brine intrusion
brine
intrusion
scenario
spent fuel
vitrified
waste
spent fuel
spent fuel
vitrified waste
spent fuel, vitrified waste, ILW
inventory
granite
clay
clay
clay
salt
salt
host rock
NRI
NRG
ENRESA
SCK∙CEN
NRG
GRS
contributor

## Slide 3: Safety indicators analyzed
Four safety indicators:
dose rate in the biosphere [Sv/a]
radiotoxicity concentration in biosphere water [Sv/m3]
radiotoxicity flux from the geosphere [Sv/a]
power density in ground water [MeV/s∙m3]

## Slide 4: Reference values
 | ENRESA | SCK∙CEN | NRG | NRI | GRS
effective dose rate [mSv/a] | 0.1-0.3 (a) | 0.3 (a) | 0.3 (e) | 0.25 (a) | 0.1(d)
radiotoxicity concentration in biosphere water [µSv/m3] | 20 (b) | 20 (b) | 20 (b) | 4 (c) | 2 (d)
radiotoxicity flux from the geosphere [Sv/a] | 60 (b) | 10 (c) | 60 (b) | 8 (c) | 0.1(d)
power density in biosphere water [MeV/s·m3] | 80 (c) | - | 80 (c) | - | 25 (c)
(a) Legal limits
(b) Reference values derived in SPIN
(c) Reference values derived in PAMINA
(d) Reference values derived in Wolf et al. (2008)
(e) IAEA recommendations (IAEA 2006)

## Slide 5: Normalized safety indicators - granite
NRI – granite

## Slide 6: Normalized safety indicators - salt
Results GRS

## Slide 7: Normalized safety indicators - salt
Results NRG

## Slide 8: Normalized safety indicators - clay
Results SCK∙CEN
Results ENRESA

## Slide 9: Normalized safety indicators - clay
Results SCK∙CEN
Results NRG

## Slide 10: Performance indicators
Six groups of performance indicators:
Performance indicators based on inventories or concentrations
  Activity / Radiotoxicity in compartments
  Activity / Radiotoxicity outside compartments
  Activity / Radiotoxicity concentration in compartment water
  Activity / Radiotoxicity concentration in biosphere water / waste package water
Performance indicators based on integrated fluxes
  Time-integrated activity / radiotoxicity flux from compartments
Performance indicators based on fluxes
  Activity / Radiotoxicity flux from compartments
Performance indicator based on safety functions
  Containment factor
  Limitation of release
  Retardation factor
  Performance of the integrated repository system
Performance indicator based on transport times
  Transport time through compartments
Other performance indicators
  Integrity of the geological barrier
  Time to plug closure

## Slide 11: Performance indicators – examples
  Indicators based on inventories or concentrations
Results SCK∙CEN - clay
Results GRS - salt

## Slide 12: Performance indicators – examples
  Indicators based on fluxes
Results ENRESA - clay

## Slide 13: Performance indicators – examples
  Indicators based on integrated fluxes
Results ENRESA - clay

## Slide 14: Performance indicators – examples
  Indicators based on transport times
Results ENRESA - clay

## Slide 15: Performance indicators – examples
  Other indicators – time to closure
Results NRG - salt

## Slide 16: Performance indicators – examples
  Other indicators – “dilatant stress state” and “fluid pressure”
Results BGR - salt

## Slide 17: Conclusions
Safety indicators
all four safety indicators give useful results with each indicator giving a different safety statement with its specific advantages
the four safety indicators together provide a much more complete picture on the repository safety than the effective dose rate alone
crucial for a safety indicator is the determination of an appropriate reference value

## Slide 18: Conclusions
Performance indicators
by transforming massive amounts of output data into a limited number of convincing indicators, performance indicators are very useful for analyzing, optimizing, and communicating repository safety
both single nuclide based indicators and indicators based on the sum of all radionuclides can be useful
time-integrated flux indicators are very illustrative but must be used with care since some aspects are not easy to understand intuitively
a plot of travel times of single radionuclides against their half lifes can be useful to show the capability of a barrier to delay and limit the release
the presentation of a combination of several performance indicators can be useful to avoid misinterpretations
in contrast to safety indicators, performance indicators are related to specific repository systems and cannot be transferred to other systems

## Slide 20: Performance indicators – examples
  Indicators based on inventory vs. transport times
Results NRG - clay

## Slide 21: Performance indicators – examples
  Indicators based on time-integrated fluxes
Results NRG - clay

## Slide 22: Performance indicators – examples
  Indicators based on inventories or concentrations
Results SCK∙CEN

## Slide 23: Performance indicators – examples
  Indicators based on fluxes
Results SCK∙CEN