## Slide 1
Uncertainty Management and Uncertainty Analysis-Review
Miguel Cuñado (Enresa)
Final Workshop Munich, September 2009

## Slide 2: PAMINA and the Safety Case
Assess the state of the art of the methodologies and approaches needed for the safety assessment of geological repositories
and
to distil the lessons learned from the rich experience accumulated in their development and application for disposal concepts in the different geological media considered in the EU Member States.
WP 1.1 Comprehensive Review of Methodologies and Approaches in the Safety Case
WP 1.2 Review of uncertainty methods and development of initial guidance

## Slide 3: Uncertainties
European Pilot Project [Vigfusson et al. 2007]:
“Uncertainties concerning the safety of repositories are unavoidable due to the complexity of the phenomena of concern and the scales in time and space under consideration, and their management is central when developing a repository system and assessing its safety”.

## Slide 4: What should be done?
Development of a management strategy involving :
a) the strategy followed in the overall repository programme to control the uncertainties which may influence the performance of the long term safety functions of the repository system; it includes the full range of actions (technical and organizational) and measures taken in the stepwise repository programme
(Uncertainty Management)
b) the actual identification and handling of the uncertainties in the safety assessment
(Uncertainty Analysis)

## Slide 5: Regulations and guidelines
[IAEA, 2006] Where there is uncertainty, it will be taken into consideration in the estimation of safety.... Furthermore, it is required that the post-closure safety case and supporting assessment identify and present an analysis of the associated uncertainties.
[SKI, 2001] requires that the following shall be reported (in the safety assessment): “how uncertainties in the description of the functions, scenarios, calculation models and calculation parameters used in the description as well as variations in barrier properties have been handled in the safety assessment, including the reporting of a sensitivity analysis which shows how the uncertainties affect the description of barrier performance and the analysis of consequences to human health and the environment”.

## Slide 6: Regulations and guidelines
[SSI, 1998] : “...the different categories of uncertainties, which are specified there, should be evaluated and reported on in a systematic way and evaluated on the basis of their importance for the result of the risk analysis.”
In France, [ASN, 1991] requests that uncertainty ranges be provided for the radiological consequences of the repository. In addition, sensitivity analysis should be carried out in order to identify priority areas for further effort, and to help in the assessment of the uncertainties affecting the results of the safety assessment.
In Finland, the Government Decision on the safety of disposal of spent nuclear fuel (478/1999) requires that “the data and models introduced in the safety analysis shall be based on the best available experimental data and expert judgement..... The uncertainties involved with safety analysis and their importance to safety shall be assessed separately”

## Slide 7: Regulations and guidelines
"Franco-Belge" document [FANC et al, 2004] states that the consideration of uncertainties is a central element of a safety case. It can be undertaken, among other ways, by the use of conventional deterministic or probabilistic uncertainty evaluation tools.
UK [Environment Agency et al, 1997] “…overall results from probabilistic risk assessments of the disposal system which explore the relevant uncertainties; suitable breakdowns of such risk assessments to show, for example, the probability distribution of doses and the contribution of important radionuclides; [and] a comprehensive record of the judgements and assumptions on which the risk assessments are based…”.

## Slide 8: Regulations and guidelines
The Czech State Office for Nuclear Safety (SUJB) issued in 2004 a methodological guide for compilation of a safety report in support of sitting application for a radioactive waste repository. This guide addresses the evaluation of uncertainties stemming from insufficient knowledge and complexity of the natural environment.
In USA (WIPP), The regulations provide the developer with a detailed, prescriptive path for the conduct of supporting assessments, and include the assessment period to be covered (10,000 years), limits on the cumulative release of radionuclides to the accessible environment, assumptions to be used in assessing particular Features, Events and Processes (FEPs), and requirements on the treatment of uncertainties.

## Slide 9: Regulations and guidelines: summary
There is an increasing attention to uncertainty management in the regulatory organizations from most countries with radwaste programs
They recognize that :
  evaluation of uncertainties is an important part of the safety assessment.
  the uncertainties should be described and handled in a consistent and structured manner.
The regulatory approach is not prescriptive (except in USA)

## Slide 10: Classification and terminology
Usually classified in three groups: (practical)
Scenario uncertainty: uncertainties associated with significant changes that may occur within the engineered systems, physical processes and site over time. [Galson D. A. et al, 2007]
Model uncertainty: uncertainties arising from an incomplete knowledge or lack of understanding of the behaviour of engineered systems, physical processes, site characteristics and their representation using simplified models and computer codes (for example, the incorrect establishment of initial conditions/boundary conditions, of the dimensionality or the level of resolution (discretisation)
Parameter uncertainty: uncertainty in the values taken by the parameters used in the models.

## Slide 11: Classification and terminology
The previous classification does not address the nature of uncertainty:
Epistemic uncertainty
  Imperfect knowledge => it could be reducible or not
Aleatory uncertainty
  irreducible
All three classes of uncertainty can contain elements that are epistemic and aleatory, but epistemic character is dominant

## Slide 12: Classification and terminology
Scenario uncertainty
  System uncertainty (SKB)
  System evolution uncertainty (Enresa)
  Future developments (NRG)
Model uncertainty
  Conceptual uncertainty (Enresa, Posiva, SKB)
Parameter uncertainty
  Numerical uncertainty (Posiva)
  Data uncertainty (SKB)

## Slide 13: Classification and terminology
Andra uses the following classification:
  Independent of the repository behaviour (e.g.: waste inventory)
  Intrinsic characteristics of the repository components (this class may be related to parameter uncertainty)
  Affecting processes controlling repository evolution:
    Affecting the prediction of long term behaviour
    Based on short term observations
    Limited validity of models (this class may be related to conceptual uncertainty)
  Technological uncertainty: a) alternative operating methods (e.g. excavation method), b) limited knowledge on the application of technologies in the underground
  External events: a) natural (tectonic, climate), b) human actions (anthropogenic effects, h. intrusion).
  Design provisions

## Slide 14: Classification and terminology
NRI and RAWRA use the following classification:
  Time uncertainty – we do not know the behaviour of barriers over thousands of years.
  Structural uncertainty – we do not know the effect of some factors (temperature, radiation, microbial) on the behaviour of barriers.
  Metric uncertainty – we do not know whether the physical of chemical data have been well determined.
  Translation uncertainty – We cannot explain causes of some effects.

## Slide 15: Methodology
Overall strategy for Uncertainty Management
  Identify, avoid, reduce, assess.
Examples of Relevant uncertainty management features that could be identified in in the national development programs
  Regulatory framework, independence of the Regulatory Authority, openness and participation of multiple stakeholders in the development process, which introduce cross-scrutiny (Enresa, NDA)
  Robust repository concept (i.e. low sensitivity to uncertainties), for example by the use of sound principles, as the multi-barrier and multi-function system, passive safety (Andra, SKB, NRG, Nagra, Enresa, SCK-CEN, ONDRAF-NIRAS).
  Intrinsically sound repository components (e.g. use of reliable materials and technologies for EBS (Andra, SKB, NDA), excellence of site characteristics (Andra, SCK-CEN, ONDRAF-NIRAS)

## Slide 16: Methodology
Basic strategies for Uncertainty Treatment
  Demonstrating that the uncertainty is irrelevant, i.e. uncertainty in a particular process is not important to safety because, for example, safety is controlled by other processes.
  Addressing the uncertainty explicitly, for example using probabilistic techniques.
  Bounding the uncertainty and showing that even the bounding case gives acceptable safety.
  Ruling out the uncertain process or event, usually on the grounds of very low probability of occurrence, or because other consequences, were the uncertain event to happen, would far outweigh concerns over the repository performance (for example a direct meteorite strike).
  Explicitly ignoring uncertainty or agreeing a stylised approach for handling an uncertainty (for example the ‘reference biospheres’ approach developed by the IAEA BIOMASS project).

## Slide 17: Methodology
Two risky approaches:
  Conservative assumptions are often the best way of addressing issues without introducing unnecessary complexity in to the models. However, this approach of making conservative assumptions can sometimes lead to models which, although robust from a safety point of view, are physically unrealistic and unlikely.
  Risk dilution. An increase in the uncertainty of the input parameters of a model (while holding the mean of the distributions constant) leads to a decrease in the mean of an output quantity. If overestimation of uncertainty results in mean consequences being reduced, the unfortunate effect is that what appears to be a conservative step (overestimating the degree of uncertainty) leads to an overoptimistic assessment of mean system performance.

## Slide 18: Conclusions
The regulations and guidance at both international and national levels identify the need for a systematic and structured management of uncertainties in the repository development programmes, and require their treatment in the safety case.
The national agencies and research organisations responsible for the repository development programmes have recognised the importance of these requirements. Experience has been gained in the application of uncertainty analysis methods in safety assessments
Both probabilistic and deterministic methods are available for uncertainty analysis. The choice between them is primarily driven by regulations. Many programmes consider that these approaches complement each other. More generally, in several programmes alternative methods are applied in parallel to increase the confidence in the results obtained.

## Slide 19: Conclusions
Aspects deserving further efforts have been identified in the various programmes. They are being actively pursued within national and international R&D programmes, in particular within Pamina RTDC2.
An uncertainty management strategy is a key element in the development of a safety case for confidence building.
High level of consensus on nature and classification of uncertainties.
Two main approaches to system PA – deterministic / probabilistic – often used together (they are complementary).
Conceptual model uncertainties least well treated in PA.
Great variety with respect to key uncertainties.
Few programmes have addressed issue of communicating.