## Slide 1
Task 2.1.C - System Approach to PA
Daniel Galson (GSL)
PAMINA Final Workshop
(Hohenkammer, September 2009)

## Slide 2: Task 2.1.C Approaches to System PA
Participants: CEA, Facilia, GSL, NRI and VTT
Research into different approaches to the quantification of uncertainty in system-wide PA calculations
  The treatment of uncertainty using probability (GSL, Facilia, VTT)
  Level of conservatism and realism in PA (GSL, Facilia)
  Hybrid stochastic-subjective approaches to treating uncertainty (NRI)
  Alternative approaches to presenting the results of probabilistic assessments (CEA) – covered by JRC presentation Task 2.1.B

## Slide 3: The Treatment of Uncertainty using Probability (Topic 1)
The use of probability offers a powerful means to treat uncertainty in PA for deep geological disposal of radioactive waste
Studies assess the advantages and drawbacks of different approaches to treating uncertainty with respect to key aspects of the safety case
GSL Topic 1 study compares total probabilistic (TSPA), partial probabilistic, and deterministic approaches
  Almost all programmes use mixture of approaches at different stages or for different purposes
  Rationale?
  Movement towards more use of partial probabilistic analysis (only some parameter uncertainties treated probabilistically)
NRI considers more exotic methods as part of Topic 3

## Slide 4: SWOT Analysis
Study uses SWOT methodology
  Strengths, Weaknesses, Opportunities, Threats
  Chosen strategy should exploit Strengths and Opportunities, and address Weaknesses and Threats
Generic analysis undertaken with reference to key elements of safety case development:
  regulatory compliance system design
  PA implementation / presentation QA
  treatment of uncertainty – all types sensitivity studies
Provides general framework for guiding decision-making on PA methodology

## Slide 5: Example – Regulatory Compliance Use of PA to demonstrate compliance with regulatory framework for geological disposal of radioactive waste
Total Probabilistic Approach
Strengths
  Unified, “one stop” approach to the treatment of uncertainty
  Results of PA can be expressed as a single value that can be compared with constraints or targets on individual dose and risk
Weaknesses
  Same approach used for all uncertainties, irrespective of importance and degree of knowledge
  Requires all uncertainties to be expressed in terms of probability distribution functions (PDFs) irrespective of type of uncertainty
  Over-reliance on numerical answers in safety case – black box effect where limitations of the analysis not respected
Opportunities
  Disaggregated results can be used for detailed analysis of system behaviour in addition to compliance demonstration
  Increasing processing power of computers will make probabilistic implementations more efficient and allow use of more complex models and/or more simulations
Threats
  There may be inadequate data for the source term, site description or evolution to quantify all uncertainties as PDFs
  Probabilistic treatment of uncertainties relating to timing of events may lead to risk dilution
  Computing resources required to achieve a converged result may lead to undue simplification of models and/or poor sampling for low-probability events
Deterministic Approach (full SWOT) Partial Probabilistic Approach (full SWOT)

## Slide 6: Treatment of Uncertainty – Generic Analysis
Most important influences on approach:
  regulatory environment
  state of programme advancement
  state of knowledge base to quantify uncertainties
Deterministic (D) or Probabilistic (P) approach?
  D tends to provide a less balanced quantitative estimate of dose or risk - may become significant as licensing approaches
  D provides clearer relationship between input and output quantities, and more focus on aspects of system where more detailed modelling is justified, e.g. for optimisation of design
  P provides quantitative statements of overall uncertainty, but requires more effort to communicate clearly, and comprehensiveness may be challenged

## Slide 7: More Detailed Generic Analyses
Generic SWOT analysis extended to consider three key areas of uncertainty:
  human intrusion
  climate change
  seismic activity
Disadvantages of probabilistic approach likely to outweigh advantages for both human intrusion and climate change
  … but does not consider regulatory environment

## Slide 8: Example – Climate Change
Probabilistic Approach
S Would allow the uncertainties and consequent effects to be included in estimates of dose/risk
W Requires the definition of PDFs - will most likely be for parameters in a very simplified conceptual model of climate change and difficult to support from observations or measurements
O A systems approach to the treatment of uncertainty allows the significance of interactions between system components to be analysed - including climate change in such an approach would allow interactions between characteristics of the climate and other parts of the disposal system to be identified and studied in more detail
T Correlations between different aspects of climate change that are not explicitly accounted for in probabilistic sampling may lead to unrealistic combinations of parameter values and potentially distort the boundary conditions for groundwater flow models
Deterministic Approach
S Calculations of dose / conditional risk for a series of deterministic climate change scenarios allow a clear comparison of the effects of different assumptions about future conditions
W Limiting the analysis of climate change to a few deterministic scenarios may not identify key interactions between parts of the disposal system or sensitivities to the timing of changes in boundary conditions
O Presenting deterministic results, e.g. as a “best estimate”, could be a useful means of communicating complex models and assumptions
T It may be difficult to present deterministic results as fully representing the complexity of the climate system

## Slide 9: SWOT Outcome - Conclusions
Provides framework for decision making and explaining PA approaches
Analysis identifies advantages and disadvantages for totally deterministic and probabilistic approaches, and for partial probabilistic approach
Generic SWOT analysis provides useful guidelines
Should be supplemented by programme-specific analysis with specific constraints

## Slide 10: Other Work in Topic 1
VTT - provided analysis specific to the Finnish programme
  treatment of rock shear, Kd, WL/Q
Facilia - compared deterministic simulation using conservative parameter estimates to the results of probabilistic simulations to illustrate the importance of considering:
  potential for over-conservatism in deterministic simulation
  spatial variability
  parameter correlation
  distribution shape
  number of probabilistic simulations
GSL – considered use of data available in statistical form to produce appropriate parameter values for deterministic PA
  best estimate (mean/median), conservative (5th/95th percentile), pessimistic (min/max)
  highly skewed distributions (log transform)

## Slide 11: Level of Conservatism and Realism in PA (Topic 2)
At what stage of repository development should assessments aim to be more conservative or more realistic?
PA is a tool for quantitative assessment of uncertainties in the safety case
One approach to the treatment of uncertainty in PA is to adopt conservative assumptions and parameter values
GSL study considers safety functions approach to PA and asks:
  Whether its use can provide a demonstrably conservative approach
  Conversely, whether its use can introduce additional, potentially unrecognised, conservatisms to a PA

## Slide 12: Study Methodology
Questionnaire & telephone interviews
  Recent experience - which safety functions are used and how derived?
  Roles of safety functions in safety case?
  Use of safety functions in communication?
  How does safety function use change as programme evolves?
  How are safety functions related to regulatory constraints?
  Is a safety functions approach to design or assessment inherently conservative or realistic?
Participants
  Belgium Switzerland
  Sweden (developer) Sweden (regulator)
  US (Yucca Mountain Project) UK

## Slide 13: Safety Function Approaches
Several approaches to using safety functions have evolved independently to deal with specific technical and regulatory requirements
  No standardised approach or methodology for using safety functions in a safety case
  No universally recognised terminology

## Slide 14: Conservatism
Using safety functions does not inherently bias the safety case towards conservatism or realism
Mechanisms identified that have the potential to introduce conservatism into the implementation
  Requiring several limits on safety function performance to be satisfied independently
    e.g., where a safety function is provided by several barriers
  Applying inappropriate limits to sub-system performance
    generic regulatory requirements
    indicators not related to overall performance measures
  Concentrating on total failure of safety functions rather than more likely gradual degradation

## Slide 15: Safety Functions & Optimisation
A safety functions approach is a valuable tool that can be used in various ways to support the analysis of the repository design/concept, and development of the safety case
However, using safety functions in a quantitative manner in optimisation studies is limited by the need to identify meaningful limits or criteria on safety function performance

## Slide 16: Avoiding Conservatism
Unintended conservatisms in a safety functions approach can be avoided by:
  Accounting for any inter-dependence of safety functions and safety function indicators
  Relating performance limits for individual safety functions to overall system performance limits
  Avoiding regulatory limits on individual safety function indicators
  Making use of additional methods for scenario development to achieve comprehensiveness (avoiding optimistic bias)
    Safety functions approach to scenario development may concentrate too much on extreme and unlikely scenarios (i.e., complete function failure) – can miss more likely scenarios related to gradual degradation

## Slide 17: Graded Approach to Modelling - Facilia Topic 2 (Conservatism & Realism in PA)
Demonstration of an approach to use generic conservative assessments to bound the scope of subsequent more realistic site-specific assessments
Allows for reduction in scope of any more realistic modelling that may be required in detailed site-specific assessments, and guidance on resource allocation
Illustrated by radionuclide screening example, based on assumed geosphere input to a reference biosphere

## Slide 18: Approach
Apply the generic screening model (Tier 2)
RQ < 1
Yes
No
Apply more realistic site-specific model
No
Yes
Apply the non-dilution model (Tier 1)
Further assessments not necessary
RQ < 1
RQ = Risk Quotient = Calc. Dose / Ref. Dose Level
Ref. dose level is set at a fraction of regulatory limit

## Slide 19: Tiers
Tier 1 is simple, and highly conservative
  Exposure over one year to entire integrated release via ingestion, inhalation and external exposure
  Model only requires dose coefficients
  No dilution
Tier 2 is more realistic, but still generic and conservative
Irrigation
LAKE
SOIL
VEGETATION
WELL
GEOSPHERE
runoff
root uptake
runoff

## Slide 20: Screening Assessment - Calculated RQs
Radionuclide | Scenario 1 |  | Scenario 2 | 
 | Tier 1 | Tier 2 | Tier 1 | Tier 2
I-129 | 5.0E+08 | 1.5E+05 | 1.6E+09 | 1.2E+06
Cl-36 | 3.1E+08 | 3.6E+04 | 1.0E+09 | 3.3E+05
C-14 | 8.2E+08 | 2.5E+02 | 0.0E+00 | 0.0E+00
Se-79 | 5.0E+02 | 1.7E-01 | 6.2E+06 | 1.7E+03
Mo-93 | 3.8E+02 | 3.5E-02 | 4.8E+09 | 7.3E+05
Pd-107 | 2.0E+02 | 7.2E-03 | 2.7E+06 | 3.3E+01
Sn-126 | 3.0E+01 | 2.3E-03 | 1.2E+07 | 4.5E+02
Nb-94 | 8.7E-03 | 4.7E-07 | 8.1E+02 | 4.2E-02
Reference Dose Level set at 1% of regulatory dose limit
Further assessment is required for radionuclides and scenarios highlighted in red

## Slide 21: Regulatory Perspective - GSL Topic 2 (Conservatism & Realism in PA)
General: all models are approximations – “realism” is relative
  Prefer “best estimate” for an analysis that attempts to mimic system behaviour
  Purpose of analysis…
Decision making –
  conservatism where yes/no answer needed
  more realistic analysis for comparison and selection of options
Demonstrating robust safety –
  conservative approach to bound uncertainty or simplify the PA
Confidence building –
  conservative analysis provides robust demonstration of safety
  more realistic analysis can be compared to observation and be used to demonstrate understanding