## Slide 1
Task 2.2.C
Scenario Uncertainty – Overview
Roger Wilmot and Daniel Galson
Galson Sciences Ltd
Notes: <number>

## Slide 2: Outline
Task Scope and Participants
Quantifying scenario probabilities
  Background
  Case studies
  Regulatory perspective
Conclusions
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer
Notes: <number>

## Slide 3: Task Scope
Traditional risk triplet
  What might happen (comprehensiveness)?
  How likely is it to happen (probability)?
  What are the consequences of it happening?
For our purposes, expanded to cover the related issues:
  How might it happen (linked with point 1)?
  How to conceptualise stylised scenarios (e.g., human action scenarios) (linked with point 2)?
There are uncertainties in all of these steps
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer
Notes: <number>

## Slide 4: Participants and Approach
Review of Scenario Development Methods:
  CEA
Review of Methods for Quantifying Scenario Probabilities:
  GSL – Overview and regulatory perspective
  VTT – Scandinavia case studies
  NRI – Czech Republic case study and formal use of expert judgement
Trial of formal use of expert judgement for scenario conceptualisation:
  NRG – Abandonment scenario
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer
Notes: <number>

## Slide 5: Background
Uncertainties are commonly classified according to whether they are:
  Parameter uncertainties
  Model uncertainties
  Scenario uncertainties
Uncertainties can also be classified according to whether they are related to:
  System uncertainties (aleatory)
  Analysis uncertainties (epistemic)
Different assessment approaches can be used to characterise and assess these types of uncertainties
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 6: Classification and nature of uncertainties
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 7: Types of scenario
Reference, main or “base case” scenario
  In deterministic assessments, assumed to have a probability of 1
Altered evolution scenarios
  Less likely, but still plausible
Bounding scenarios
  Extreme events, still within range of realistic possibilities
“What if” or residual scenarios
  Highly implausible or impossible, nominal probability of zero
Stylised scenarios
  Few or no relevant data and very large uncertainties, such that probability is considered meaningless
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 8: FEP and scenario uncertainties
Scenarios may be defined according to the occurrence (or non-occurrence) of a FEP
Uncertainties about the FEP occurring (scenario uncertainty) are different to uncertainties about the characteristics of the FEP (parameter uncertainties)
The probability of scenarios can be discussed in the SC
  Quantitatively
  Qualitatively
  Not at all (stylised scenarios)
Quantitative evaluation of uncertainties may use a deterministic or a probabilistic approach
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 9: Review of Methods for Quantifying Scenario Probabilities
Review topics
  For which scenarios (events) is probability determination feasible?
  Examples of use
  What techniques are generally available for probability quantification?
  For which scenarios (events) should probability determination not be attempted and why?
  For which scenarios (events) is stylisation necessary and why? How has this been done?
Case Studies
Regulatory Perspective
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer
Notes: <number>

## Slide 10: Review of Methods for Quantifying Scenario Probabilities
Question 1: For which scenarios (events) is probability determination feasible?
  Sufficient frequency data are available and projection into the future is considered reasonable
  Sufficient data are available to generate a realistic probability density function (PDF) for a well understood physical system
  If the event or process is considered to be random, sufficient data are available to demonstrate randomness and a likelihood of future randomness
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 11: TSPA Case Studies
US Yucca Mountain and Waste Isolation Pilot Plant (WIPP) Total System Performance Assessments (TSPAs) use PDFs for parameters that
  Characterise relevant FEPs
  Define the probability of occurrence of scenarios
WIPP
  Undisturbed performance, mining, drilling
Yucca Mountain
  Nominal, early EBS failure, igneous, seismic
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 12: Partially probabilistic case studies
Swedish and Finnish PAs for KBS-3 Disposal Concept
Reference case assigned a probability of one and alternative scenarios are described as less likely or residual scenarios
Numerical values estimated for probability of scenarios involving rock shear, and an earthquake of sufficient size to damage canisters
Where data are insufficient, the probability of a scenario occurring is set to one, even if probability is considered to be low
Vieno and Nordman, 1999
<number>

## Slide 13: Review of Methods for Quantifying Scenario Probabilities
Question 2: What techniques are available for probability quantification?
  A reference case comprises all FEPs that are certain to occur – probability of one
  Altered evolution or other less likely scenarios include FEPs that are not certain to occur. In deterministic PAs, the probability may be set to one and the significance of conditional doses or risks judged using a qualitative assessment of likelihood
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 14: Deterministic case study
In the Swiss (Nagra) Opalinus Clay PA, the reference case is given a probability of one, and separate cases are considered as variant scenarios, which are also given a nominal probability of one
Nagra, 2002.
<number>

## Slide 15: Review of Methods for Quantifying Scenario Probabilities
Question 2 (cont.): What techniques are available for probability quantification?
  If the probability of “scenario-forming” FEPs can be reasonably determined, the probability of the scenario can be defined, potentially using one of the following approaches:
    Derivation from observations of past events and existing conditions
    Sampling a model of the physical system using Monte Carlo simulations
    Use of a probability model (e.g. Poisson)
    Use of expert judgement, ideally through a formal elicitation process
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 16: TSPA Case Studies
Scenario probabilities based on analysis of the frequency of previous events and expert judgement
  Example of a logic diagram used to determine probability of volcanic event intersecting the proposed repository at Yucca Mountain
Crowe et al., 2006
<number>

## Slide 17: Review of Methods for Quantifying Scenario Probabilities
Question 3: Under what circumstances should probability estimation not be attempted and why?
Case Studies:
  In the UK, the environmental regulators state that uncertainties (including through estimation of probabilities) should be quantified only where this is justifiable through statistical evaluation or other means.
Environment Agency and NIEA, 2009
<number>

## Slide 18
Case Studies:
  Consistent with ICRP guidance, no attempt is usually made to quantify the probabilities of human-induced scenarios (the US WIPP project is an exception due to its location in a resource-rich area)
  If regulatory siting requirements exclude areas where natural events could significantly affect the disposal system, limited value in detailed quantification of probability
  If consequences of a scenario do not significantly affect calculated performance, limited value in detailed quantification of probability
  Residual or “what if” scenarios have a very low probability of occurrence and are generally assigned a probability of zero. Used to illustrate the robustness of barriers or the overall disposal system
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 19: Review of Methods for Quantifying Scenario Probabilities
Question 4: For which scenarios is stylisation necessary and why?
Stylised assumptions are generally applied to scenarios involving future human actions because of the large uncertainties involved in predicting the future evolution of society. Notable differences between programmes result from differences in regulations:
  Regulators in Europe consider that the developer/operator of the disposal system should use stylised assumptions to explore future human action scenarios (Vigfusson et al., 2007).
  In contrast, for the US WIPP project, the regulator specified the assumptions and calculation processes to be used in developing human intrusion scenarios, based on historical data, and a stylised approach was not necessary.
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 20: Regulatory Perspectives
In the US, regulations tend to be prescriptive, specifying that repository developers/operators must conduct probabilistic assessments, the assumptions to be made and the methods to be used
In Europe, repository developers/operators are encouraged to develop a limited number of illustrative scenarios to enhance understanding of the disposal system and its evolution. Both deterministic and partial probabilistic methods are accepted by the regulators
  Some concerns expressed about use of fully probabilistic TSPA for decision-making
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer

## Slide 21: Conclusions: Enhancing credibility
Careful interpretation of data in the geological / historical record
Careful explanation that most scenario probabilities are “degrees of belief” rather than relative frequencies
Formal expert judgement where safety case outcome relies significantly on assessments of scenario probability
Simplify assessments and identify factors that could affect estimates of scenario probability
Avoid probability estimation where insufficient information is available, or is otherwise avoidable
<number>
PAMINA Final Workshop 28 - 30 September 2009, Hohenkammer
Notes: <number>