## Slide 1
PAMINA Final Workshop, September 28-30, 2009 Hohenkammer, Germany
Probabilistic Safety Assessment
Pilot Study on PSA
Gerhard Mayer, AF-Colenco

## Slide 2: Contents
Introduction
Tools for deterministic RN calculation
Probabilistic tool: @RISK
Application to High Level Waste Repository
  Reference Conceptualisation
  RN release affected by ramp / shaft
Conclusions
Report NAB 07-09 (in German) available at NAGRA

## Slide 3: Toolbox for deterministic RN release calculations
STMAN
  Release of dissolved RN from near field
PICNIC
  Transport of dissolved RN through geosphere
TAME
  Biosphere compartment model
Near field
calculation
RN Inventory
Geosphere
calculation
Biosphere
calculation
Dose

## Slide 4: Toolbox for deterministic RN release calculations
Each Tool is well tested
Combination of tools gives high flexibility
Adjustable level of detail
  Simplified  Fast
  Detailed  Slow
Toolbox does not cope with all identified FEPs
(Toolbox has been extended)

## Slide 5: Requirements for probabilistic tool
Definition of probabilistic distribution functions
Generation of realizations
Calculation of RN release  Toolbox for RN release calculations
Statistical analysis of results

## Slide 6: @RISK
Commercial Excel add-in
Definition of Probabilistic Distribution Functions
Sampling
   Monte Carlo
   Latin hypercube
Statistical analysis
   Time series
   Convergence Monitor
Interfacing with Toolbox for RN release calculations by reading and writing XML-files using VBA

## Slide 7: Workflow
@RISK
PDFs
input0001.xml
input0002.xml
...
output0001.xml
output0002.xml
....
RN Release Toolbox
RN Release Model
1. Define Model
2. Calculate
Run Monte Carlo Simulation
Rerun Monte Carlo Simulation
Statistical Analysis
3. Analysis
Model
template
RN Release calculations
on Linux cluster

## Slide 8: Application: Max. Dose from a High Level Waste Repository in Opalinus Clay
Processes considered
  Time dependent release from waste packages
  Transport of dissolved RN due to advection, dispersion/diffusion
  Sorption
  Solubility limitation
Not considered here:
  Release of volatile RN
  Effects of gas generation
  Coupled processes (HM, THM, THMC…)

## Slide 9: Application: Max. Dose from a High Level Waste Repository in Opalinus Clay (II)
Probabilistic parameters of near field
Spent Fuel
  Instant release fraction (IRF) and matrix dissolution rate
  Diffusion Coefficients in bentonite buffer
  Kd-Values in bentonite buffer
  Solubility limits
Vitrified high level waste
  Glass dissolution rate
  Diffusion Coefficients in bentonite buffer
  Kd-Values in bentonite buffer
  Solubility limits
Intermediate level waste
  Kd-Values in cemented waste
  Solubility limits
Probabilistic parameters of geosphere
Darcy velocity in host rock
Diffusion coefficients
Kd-Values
Transport path length
In total: 176 Parameters

## Slide 10: SF Reference Case (Deterministic)

## Slide 11: SF, 1000 samples

## Slide 12: SF, HLW, ILW: CCDF

## Slide 13: Correlation of parameters with max. total dose
Darcy velocity in host rock
Instant release fraction of Iodine
Sorption coefficient of Iodine in host rock
Diffusion coefficient in host rock
Transport path length in host rock
176 parameters have been diced
About 5 are sensitive

## Slide 14: 10, 100, 1000, 10000, … How many samples are required?
Approach: Stop sampling when Statistics change < X %
Statistics used by @RISK
  Percentile
    0-5%, 5% -10%, …,95%-100%
  Mean
  Standard deviation of mean
Calculate statistics
Run S
Stop Sampling
S = 1
Statistics change
< X% ?
Yes
No
S+1

## Slide 15: Convergence Monitor

## Slide 16: How many samples are required?
Convergence criterion | Number of samples | Mean Maximum Dose [mSv/a]
14 % | 100 | 4.14.10-5
2 % | 220 | 4.75.10-5
1 % | 370 | 4.74.10-5
0.5 % | 660 | 4.68.10-5
0.4 % | 1000 | 4.68.10-5

## Slide 17: RN release affected by ramp / shaft
Dose contribution from pathway ramp / shaft is negligible
Log(Max. Dose) [mSv/a]
Host rock
Ramp / Shaft
CCDF

## Slide 18: How long does it take?
One sample:
  5 x Near field -> 5 minutes
  3 x Geosphere -> 3 minutes
  3 x Biosphere << 1 minute
Total: 7-8 minutes / sample
Using cluster with 10 Quad Core CPUs
Total: 3 hours for 1000 samples

## Slide 19: Conclusions
Probabilistic Safety Analysis gives valuable insight in system behavior
Maximum Dose of the investigated repository system affected by a few parameters only (consistent with experience from deterministic calculations)
Calculation time for a probabilistic performance analysis is fair
Extension of Toolbox for RN release calculations required to cope with all identified FEPs
@RISK can be used for Monte Carlo Simulations
The functionality provided by @RISK for stochastic analysis is limited