## Slide 1
Sensitivity analysis (SA) Review
Sabine M. Spießl
Notes: <number>

## Slide 2: Outline
<number>
Introduction and background
  Types of uncertainties
  Terminology
  Increased interest in SA
  SA approaches
Regulations and guidelines
Methodology
  Sampling
  Methods and techniques
Application examples from the different participating organisations
Conclusions
Notes: <number>

## Slide 3: Introduction and background
<number>
Types of uncertainties
  Aleatory (variability, stochastic or irreducible) uncertainties
    known as randomness, unpredictability or variability of the system, e.g., variability in environmental conditions like weather conditions
  Epistemic (knowledge, subjective or reducible) uncertainties
    results from the existing state of knowledge about the system, its parameters as well as about available and feasible model concepts
On uncertainty
"That is what we meant by science. That both question and answer are tied up with uncertainty, and that they are painful. But that there is no way around them. And that you hide nothing; instead, everything is brought out into the open“
Borderliners, Peter Høeg, Delta publisher, 1995
Notes: <number>

## Slide 4
<number>
Terminology
  Uncertainty analysis
    An analysis to estimate the uncertainties and error bounds of the quantities involved in, and the results from, the solution of a problem (IAEA Safety Glossary)
  Sensitivity analysis (SA)
    Is the study of how the variation in the output of a model can be apportioned to different sources of variation, and of how the given model depends upon the information fed into it (Saltelli)
    A quantitative examination of how the behaviour of a system varies with change, usually in the values of the governing parameters (IAEA Safety Glossary)
Most participating organisations stick more or less to these definitions.
Introduction and background
Notes: <number>

## Slide 5: Introduction and background
<number>
Why is there an increased interest in SA?
  Improvement of system understanding
  Identification of ‘critical’ parameters
  Need to identify degree of output uncertainties as result of input parameters
  Necessity of transparency
  Establishment of priorities for research
“Uncertainty cannot be resolved into certitude in most instances. Instead, transparency can be offered by sensitivity analysis. Transparency is what is needed to ensure that the negotiating parties do not throw away science as a just another contentious input.”
Wresting Environmental Decisions From an Uncertain World
by Pasky Pascual, Environmental Law Institute®, Washington, DC. reprinted with permission from ELR®, 1-800-433-5120, ELR NEWS&ANALYSIS, 8-2005 35 ELR 10539.
Notes: <number>

## Slide 6: Introduction and background
<number>
SA approaches
  Deterministic SA
    Used to investigate the model output under the variation of a single or several parameters, model modifications, scenarios or assumptions
  Probabilistic SA
    Is mostly to analyse the model sensitivity against parameter uncertainties
    Entire parameter space is explored
    Parameters follow a statistical distribution, e.g. uniform, log normal
    A large number of parameters can be varied within a set of simulations
  Local SA
    Investigation of only a small vicinity of a specific point in the parameter space
    Often, deterministic SA are used for local SA
  Global SA
    Consideration of the entire parameter space
    Investigation of parameter interaction
    Probabilistic SA are frequently used for global SA
Notes: <number>

## Slide 7: Regulations and guidelines
<number>
Generally, regulations for SA are not very specific and rather inhomogeneous between the European countries
New guidelines are being developed by several countries
Germany:
  BMU: Safety Requirements Governing the Final Disposal of Heat-Generating Radioactive Waste, July 2009
  In the framework of numerical assessment of long-term safety, SA is required in order to highlight the potential solution space and be able to estimate the influence of uncertainties
France:
  Guidance: Basic Safety Rule 3.2.f – demonstration of safety through evolution scenarios
  New version in 2007: notions and safety approaches developed in the 2005 Clay Dossier. Requirement: identification of most important parameters by SA
Notes: <number>

## Slide 8: Regulations and guidelines
<number>
United Kingdom:
  GRA: Guidance on Requirements for Authorisation is being revised
  SA is not explicitly required by GRA, but a requirement indicates that a safety case is not depended unduly on any single component
  The draft of GRA places a strong emphasis on the importance of optimisation
Czech Republic:
  Safety report for site licensing of DGR in 2004: uncertainty of results should be evaluated by SA
Belgium:
  Regulatory requirements and guidelines in preparation
The Netherlands, Finland and Spain:
  Currently no valid regulations
Notes: <number>

## Slide 9: Methodology for probabilistic SA
<number>
Sampling
  Procedure for generating a set of parameter values on the basis of parameter distribution
  Easiest and most popular used: random sampling
  Latin Hypercube Sampling (LHS): parameter interval is divided into sub-intervals of equal integral probability to ensure that parameter values are spread over the whole range of their distribution
  FAST sampling: periodic scan of the parameter space with well-defined frequencies
SA methods
  Correlation- and regression-based methods
  Non-parametric statistical test
  Variance-based methods (FAST and SOBOL)
  Graphical methods
Notes: <number>

## Slide 10: SA methods – Correlation and regression methods
<number>
Best suitable for models with a close-to-linear behaviour
Correlation (PEAR, SPEA) tests: based on an analysis of the linear correlation between the model output and the input parameters
Regression (SRC, SRRC) tests: based on the calc. influences of the individual input parameters to a linear regression of the output values
Both methods are closely interrelated and yield similar results
SPEA and SRRC are rank-based tests for highly non-linear but monotonic models
  Significant improvement of coefficient of model determination
  Transformation of monotonic relations to linear relations
  Normally more robust and reliable results for the price of losing quantitative meaning
PEAR = Pearson coeff.
SPEA = Spearman coeff.
SRC = standardised regression coeff.
SRRC = standardised rank regression coeff.
Notes: <number>

## Slide 11: SA methods – Correlation and regression methods
<number>
PCC and PRCC tests for correlated input parameters
  PCC is the ordinary correlation coefficient between the residuals of two linear regression models which were constructed (one for the input parameter under investigation and one for the output variable, each with respect to all input parameters except that one under investigation)
PCC values ≡ SRC values if parameters are uncorrelated
PRCC values ≡ SRRC values if parameters are uncorrelated
PCC = partial correlation coeff.
PRCC = partial rank correlation coeff.
SRC = standardised regression coeff.
SRRC = standardised rank regression coeff.
Notes: <number>

## Slide 12: SA methods – Non-parametric statistical tests
<number>
Sample is divided into 2 subsamples according to some criterion, then it is checked whether the results of the two subsamples differ significantly
Cramér – von Mises, Kruskal – Wallis, Mann – Whitney and Smirnov tests
Notes: <number>

## Slide 13: SA methods – Variance-based methods
<number>
Also applicable to non-linear and non-monotonic systems
Calculation of quantitative measure for the sensitivity of the output
  first-order sensitivity index (isolated influences of individual parameters)
  total-order sensitivity index (influences of parameters in interaction with all others)
SOBOL indexes: decomposition of the total variance into terms of increasing dimensionality
  yields not only first- and total order sensitivity index but also higher order indexes
FAST indexes: as SOBOL indexes but parameter space is periodically explored with interference-free frequencies and output is analysed by means of a Fourier analysis
  Only first- and total order sensitivity index
High number of model runs necessary
Notes: <number>

## Slide 14: SA methods – Graphical methods
<number>
Scatter plots (show directly how the system reacts to the variation of a specific parameter)
Cobweb plots
Cumulative sample mean (CSM) plots
Cobweb and CSM plots illustrate the main influences on the model output in one figure
Notes: <number>

## Slide 15: Application examples (Spanish group - ENRESA)
<number>
Deterministic results
Groups of variants in different compartments of the repository
Notes: <number>

## Slide 16: Application examples (Czech group – NRI/RAWRA)
<number>
Deterministic SA studies
  DGR programme
  A lot of calculations
effect of backfill thickness on flux 238U from backfill
Notes: <number>

## Slide 17: Application examples (French group - ANDRA)
<number>
Deterministic studies
SA studies
of the normal
evolution scenario
in the framework
of the
Dossier 2005 Argile
Notes: <number>

## Slide 18: Application examples (Finnish group – POSIVA)
<number>
Deterministic SA studies within TILA-99
  what-if cases
    a combination of very high flow of non-saline groundwater (vhflowns) and saline groundwater chemistry
    very poor performance of bentonite
    displacement of contaminated water out of the canister due to gas generation
    glacial meltwater
    postglacial faulting
Notes: <number>

## Slide 19: Application examples (Belgian group – SCK•CEN and ONDRAF/NIRAS)
<number>
Probabilistic results (time depended - PRCC test)
effective thickness
of the clay barrier
solubility of Se
migration parameters (diffusion coefficient and retardation factor) of Sn
I-129
Cl-36
Sn-126
Notes: <number>

## Slide 20: Application examples (Dutch group - NRG)
<number>
SA in PROSA
  Salt compartment (groundwater intrusion and a subrosion scenario)
  Groundwater travel time
  Dose conversion factors
  3 rank-based correlation or regression methods (SPEAR, PRCC and SRRC)
  Smirnov test
Sensitivity coefficients for the subrosion model
Notes: <number>

## Slide 21: Application examples (German group – GRS Braunschweig)
<number>
Probabilistic results (time depended -FAST first order SA index)
No satisfying robustness, even with more than 10000 runs
Notes: <number>

## Slide 22: Application examples (German group – GRS Köln)
<number>
Probabilistic SA studies (small number of simulations)
  Performance assessment for the Konrad LLW/ILW site
  UTD project (disposal mines for chemically-toxic waste)
Notes: <number>

## Slide 23: Application examples (UK group – NDA)
<number>
SA studies
  Post-closure safety case (NIR 97)
  70000 sensitivity calculations
Notes: <number>

## Slide 24: Application examples (French group - IRSN)
<number>
IRSN
  Mainly works for the regulator
  Follows the recommendations of ASN (Nuclear Safety Authority)
    To define situations that are likely to occur in a normal evolution scenario
    To explore altered evolution cases in order to test the sensitivity
Notes: <number>

## Slide 25: Conclusions
<number>
All organisations agree that SA is an important part of the performance assessment for radioactive waste repositories
Applied SA methods by the different organisations vary considerably
Most organisations prefer probabilistic SA since the parameter space is better explored
Most used correlation- or regression-based methods
Also advanced methods (FAST) were applied
Notes: <number>

## Slide 26: Thanks for your attention
<number>
Notes: <number>