## Slide 1
“Fully” probabilistic safety assessment: Regulatory situation (PAMINA 2.2.E)
PAMINA Final Workshop September, 28 - 30 2009, Hohenkammer, Germany
K.-J. Röhlig, E. Plischke (TUC)

## Slide 2: Outline
Motivation / introduction
Regulations and fully probabilistic assessments
“Fully” probabilistic assessments: Review of selected cases
Summary / conclusions

## Slide 3: Motivation / introduction
Quantitative statements about uncertainties and their effects in PA desirable
Traditionally and due to the well-developed toolbox: probabilistic approaches most often used (Despite ongoing discussions about adequacy and legitimacy and on the value of other mathematical methods, e.g. interval analysis, fuzzy arithmetic, possibility theory, …)
Wide variation with regard to nature and range of uncertainties being addressed by probabilities or probability density functions
Rarely: “all” uncertainties addressed probabilistically
Strictly spoken, each otherwise probabilistic assessment can be considered based on a “combined” (deterministic-probabilistic) approach
Our subject: assessments in which this is not (or almost not) the case  “fully” probabilistic assessments
Idea: 80ies and 90ies – B. Thompson – “Dry Run 3” exercise undertaken by a regulator(!) and driven by regulatory situation
Notes: by “deterministic” we mean the exploration of selected uncertainties by performing calculations according to designs developed in a “targeted” way. The assessor asks specific questions and performs a limited number of calculations in order to address these questions. Thus, he acts “locally”.
In contrast, there are “global” methods which aim at exploring the whole space of quantifiable uncertainties at the same time, thus specifically asking for the effects of combinations of uncertainties. Interval analysis, fuzzy arithmetic, possibility theory and others might be theoretical bases for such methods but if such a method is based on the assumption that the uncertainties under consideration can be expressed by probabilities or probability density functions, we call it “probabilistic”.
Thus, we would call assessments according to a fractional factorial design “deterministic” or “local”, assessments using a full factorial design “global”, but not “probabilistic”. Accordingly, latin hypercube designs, if using probabilities or probability density functions, would be called “probabilistic” even if they were based on median (i.e. deterministically chosen) values for the parameter intervals under question.

## Slide 4: Motivation / introduction (2)
Since then: several PA’s/SA’s more or less “fully” accounting for uncertainties by means of probabilistic approaches
  “Total System Simulation”
  “Environmental system simulation”
  “System Simulation Approach”
  “Probabilistic System(s) Assessment (PSA)”
PAMINA:  previous presentations
This presentation: Milestone 2.2.E.5
  Summary: rules and regulations with a view to their compatibility with “fully” probabilistic approaches and their potential to encourage or discourage such approaches
  Compilation & evaluation from a regulatory perspective : existing “fully” probabilistic SAs.
  Discussion
Notes: by “deterministic” we mean the exploration of selected uncertainties by performing calculations according to designs developed in a “targeted” way. The assessor asks specific questions and performs a limited number of calculations in order to address these questions. Thus, he acts “locally”.
In contrast, there are “global” methods which aim at exploring the whole space of quantifiable uncertainties at the same time, thus specifically asking for the effects of combinations of uncertainties. Interval analysis, fuzzy arithmetic, possibility theory and others might be theoretical bases for such methods but if such a method is based on the assumption that the uncertainties under consideration can be expressed by probabilities or probability density functions, we call it “probabilistic”.
Thus, we would call assessments according to a fractional factorial design “deterministic” or “local”, assessments using a full factorial design “global”, but not “probabilistic”. Accordingly, latin hypercube designs, if using probabilities or probability density functions, would be called “probabilistic” even if they were based on median (i.e. deterministically chosen) values for the parameter intervals under question.

## Slide 5: Regulations and fully probabilistic assessments
Current national regulations less focussed and less prescriptive on assessment issues than older ones
More emphasis on other, more general issues (safety case in general, technical requirements, optimisation, BAT, …
But numerical compliance still considered central (cf. next slide about calculation endpoints)
Requests to appropriately address uncertainties – 3 approaches (M1.2.1 ):
  1. Prescribed methods for the treatment of uncertainty (US)
  2. Detailed regulatory guidance with only objectives defined (majority)
  3. No particular national guidance (?)
Varying attitude towards probabilistic assessment methods
Not an issue in IAEA Safety Requirements WS-R-4, but Draft Safety Guide DS355 (under development) will most likely advocate a combination of deterministic and probabilistic techniques

## Slide 6: Criteria concerning calculation endpoints (a.k.a. primary performance measures, safety indicators)
Review basis: LTSC compilation (NEA 2007) & more recent developments
Dose or risk? (Or a combination, or something else, e.g. STUK regulations)
Perception: dose  deterministics, risk  probabilistics not necessarily true!
  Dose in probabilistic assessments: problems if (as to be expected) some realisations lead to results violating the numerical criteria and if the regulation does not account for such a possibility
  Example of dose-based regulation accounting for this issue: Yucca Mountain („reasonable expectation“)
  risk: not a problem even if regulation does not explicitly mention probabilistics (interpretation risk = mean)
  informed regulator will ask for variation, uncertainty, risk dilution and related issues even if these are not addressed in written regulations
  risk criterion: not necessarily request for a probabilistic assessment: risk estimate solely based on deterministic calculations is possible

## Slide 7: Regulatory issues: Risk
Risk dilution (addressed e.g. in Swedish regulations)
Concern: high probability/low impact and low probability/high impact scenarios are attributed to the same level of risk
  more relative weight to higher consequences???

## Slide 8: Regulator will only be satisfied if …
Assessment and documentation enables to understand where the uncertainties comes from and what their implications are
  well-structured documentation
  disaggregated presentation of results even in the case of a “fully” probabilistic assessment – no “Black boxes”!
He can be reasonably assured that the “uncertainty space” (including correlations, dependencies, and interactions) has been reasonably well explored
  Probabilistic assessment certainly helps
  But keep it manageable and understandable (“the fuller the better” – but there are limits …)
  If pdf’s / likelihoods not sufficiently well justified: Probabilistics still valuable – informs about uncertainty space. Open: If/ how to address in regulations. Might be a problem in regulatory environments focussed on formal compliance  detailed regulations (e.g. on scenarios, likelihoods, statistics to be used etc.) as way out? But – too prescriptive?

## Slide 9: Review of selected cases: Questions asked
Aim and purpose of the assessment?
Regulatory environment?
Scenarios ? How developed? How were likelihoods of occurrence derived? How was completeness or comprehensiveness substantiated?
Model uncertainties – how addressed?
Probabilities / pdfs – how derived and justified?
Risk dilution?
Audience / presentation?
Regulator’s reply?

## Slide 10: Review of selected cases: Assessments considered
“Dry Run 3” (UK HMIP, early 90ies): First attempt to thoroughly perform a fully probabilistic assessment. Probably the most consequent implementation of a fully probabilistic assessment.
WIPP certification and re-certification (U.S. DoE, 1996 & 2004): Particular approaches to deal with aleatory and epistemic uncertainty in probabilistic assessments. Specific regulatory environment
Yucca Mountain license application (U.S. DoE, 2008): dto.
SR-Can (SKB, 2006): Risk criterion, but assessment approach combining deterministic and probabilistic methods. Rather heavily relying on probabilistic techniques. Model uncertainties.
No (except for Dry Run 3”) “really full” probabilistic assessments!

## Slide 11: HMIP Dry Run 3

## Slide 12: HMIP Dry Run 3

## Slide 13: SR-Can: A recent assessment combining deterministic and probabilistic techniques in a risk-based regulatory environment
“copp_corr” and “shear”: scenarios n: number of realisations considered for each scenario c: calculated doses pshear : probabilities for shear failure (derived on the basis of earthquake probabilities, fracture detection probabilities and probabilities for fractures intersecting canisters) Probability for the copper corrosion scenario: overestimated with 1
epistemic and aleatory uncertainty concerning hydrogeology addressed by
  one-by-one usage of alternative models concerning hydraulic rock properties,
  probabilistic runs addressing spatial variability based on pessimistic, average, and favourable values, respectively, for the epistemic uncertainties

## Slide 14: SR-Can: A recent assessment combining deterministic and probabilistic techniques in a risk-based regulatory environment

## Slide 15: Summary and conclusions
Attempt to shed light on the role of regulations and regulatory expectations in relation to the application, applicability, and acceptability of so-called fully probabilistic assessment approaches
Areas of interest:
  Degree to which (written) regulation prescribes / requires (or otherwise) the application of such methods
  Regulatory review process during which such an assessment will undergo scrutiny
  General methodological issues

## Slide 16: Summary and conclusions: Regulations prescribing (or otherwise) methods
Almost all national regulations belong to type “Detailed regulatory guidance with only objectives defined”. Exception U.S., especially WIPP
Role of calculation endpoints:
  dose-based criteria should avoid language which prevents from exploring the uncertainty space due to the fear that some calculations might yield results exceeding the criterion
  risk-based criteria should not be limited to requesting the presentation of mean values but encourage to address the whole uncertainty space

## Slide 17: Summary and conclusions: Regulatory review process
Informed regulator will ask for
  variation
  uncertainty in results
  risk dilution
  etc.
… even if these issues are not addressed in written regulations
Necessity for the applicant to disaggregate the presentation of results even in cases in which written regulations do not require such disaggregation
Probabilistic assessments: high interest to learn about the full result distribution including statistics other than mean values, e.g. percentiles etc.

## Slide 18: Summary and conclusions: General methodological issues
Not always clear: what is a “fully” probabilistic assessment: “Conventional” probabilistic assessments = restricted to parameters for which a pdf can be derived reasonably well (“aleatory uncertainty”). Possible extensions:
  pdf’s for parameters without sufficient statistical basis (“epistemic uncertainty”), i.e. by formal expert elicitation  other PAMINA WP (but note U.S. regulatory requirements – aleatory and epistemic uncertainties
  scenario (“temporal”) uncertainty  likelihoods of scenario occurrence  next slide
  alternative conceptualisations and modelling approaches
    WIPP: indicator variables
    SR-Can: deterministic treatment systematically incorporated into a probabilistic framework
    Previous presentations

## Slide 19: General methodological issues: Scenario uncertainty
“Scenario approach” ↔ “full” probabilistics no longer an antagonism
To be completely probabilistic: neither feasible nor necessary
SR-Can: possibility of being comprehensive (scenario development based on safety functions) and of combining deterministic and probabilistic methods in a risk-based regulatory environment
Quantification or quantifiability: decisive for choice of approaches
Degree of aggregation: Common sense!
  But restrictively addressed in U.S. regulations
  “lumping”: pdf’s, dependencies, correlations, interactions well-known. Even if not: Explore full uncertainty space but take probability statements with care (compliance?)
  “splitting”: cases / sub-spaces with unknown or low (statistical confidence!) probabilities, demonstration / repository development.
Do “fully” probabilistic assessments really circumvent the problems of looking for conservative data?  further to be investigated
Toolbox of stochastic processes: potentials to be explored