## Slide 1
Sensitivity Analysis – New Developments
Case Studies
WP 2.1.D

## Slide 2: Scope of the Work
Application of different probabilistic Sensitivity Analysis methods to realistic repository system models
  Correlation and regression methods
    value-based
    rank-based
  Non-parametrical statistics / MC filtering
  Graphical methods
  Variance-based methods
6 model systems investigated
  2 salt (NRG, GRS)
  2 clay (NRG, JRC/ANDRA)
  1 granite (ENRESA)
  1 biosphere model (Facilia)
Different PA tools applied
Objectives
  Testing of different SA methods on realistic systems with complex behaviour
  Comparing different methods
  Identification of specific problems

## Slide 3: Overview of the Applied Methods (1)
Sampling
  Probabilistic global SA requires a big number of model runs with varied input parameters
  Parameter values are drawn according to their PDFs
  Random sampling
    Apply a quasi-random algorithm
  Latin Hypercube sampling (LHS)
    Divide the parameter intervals in sub-intervals of equal probability
    Draw one (or more) values in each interval
  Specific sampling
    Necessary for some SA methods (e.g. FAST sampling)

## Slide 4: Overview of the Applied Methods (2)
Correlation coefficients
  Calculate the statistical correlation between input parameter and model output
  Coefficients are a measure for the sensitivity of the model to the parameter
Standardised regression coefficients
  Perform multilinear regression
  Coefficients are a measure for the sensitivity of the model to the parameter
Partial correlation coefficients
  Technique to exclude effects of other variables
  Identical to standardised regression coefficients if the input variables are uncorrelated
These methods perform best with close-to-linear systems
Can be checked by calculating the coefficient of model determination: R²
R² should be greater than 0.5

## Slide 5: Overview of the Applied Methods (3)
Rank transformation
  Order the values of input and output parameters
  Replace the values by their ranks in the ordered lists
  Transforms monotonicity to linearity
Rank transformation often improves the performance of correlation and regression-based SA methods
but reduces the quantitative meaning of the coefficients

## Slide 6: Overview of the Applied Methods (4)
Monte-Carlo filtering
  Non-parametrical statistical tests
    Smirnov test
    Mann-Whitney test
    t-test
  Sub-divide samples in two according to highest output
  Compare sub-samples using specific methods
Applicable to all kinds of models
but sometimes hard to interpret

## Slide 7: Overview of the Applied Methods (5)
Variance-based methods
  Calculate the fraction of the output variance that is due to the variance of a specific input parameter
  First-order and multi-order sensitivity indices
    describing coupled influences
  Different methods available
    Sobol’, FAST, RBD, …
  Specific sampling necessary
Adequate for non-linear and non-monotonic models

## Slide 8: Overview of the Applied Methods (6)
Graphical methods
  Scatter plots
    plot output vs. one input parameter
    quick qualitative information on sensitivity
  Cobweb plots
    draw connecting lines between ranks of input parameters and output
    quick identification of most relevant parameters
  CSM plots
    order the sample according to one parameter
    calculate relative contribution to sample mean (CSM) for each value
    plot CSM against parameter value
    relevant parameters show significant deviance from straight line

## Slide 9: Overview of the Case Studies
Study | Input Params | Runs | Methods |  |  |  | 
 |  |  | Corr./Regr. |  | MC-Filtering | Variance-based | Graphical plots
 |  |  | Value | Rank |  |  | 
NRG salt | 6 | 1000 | PEAR, SRC, PCC | SPEA, SRRC, PRCC |  |  | Scatter
NRG clay | 3 | 499 | SRC | SRRC | Smirnov, M-W |  | CSM, Cobweb
GRS salt | 6 | 3030-6054 | PEAR | SPEA | Smirnov | EFAST | Scatter, CSM, Cobweb
Enresa granite | 135 | 200 – 25000 | PEAR, SRC | SPEA, SRRC | Smirnov, M-W, t |  | CSM
JRC/Andra clay | 24 | 1000 | (SRC) | SRRC |  |  | 
Facilia biosphere | 26 | 10000 | PEAR, SRC, PCC | SPEA, SRRC, PRCC |  | Sobol‘, EFAST | 

## Slide 10: NRG: Generic repository design in rock salt
Dutch concept with the option of retrievability
Torad-B vertical borehole concept
vitrified HLW in COGEMA canisters
boreholes
300 canisters per borehole (500 m deep )
sealing plugs of compacted salt grit
Focus on: compaction behaviour of rock-salt plug
Models for creep rate and for permeability-porosity relation of rock salt verified with experimental data
Models implemented in EMOS
Uncertainties in model parameters identified
6 variable input parameters: statistical distributions assumed
Uncertainty/sensitivity analysis: 1000 EMOS runs

## Slide 11: Permeability evolution of rock-salt plug
Runs terminated by EMOS at different times
As time increases, less and less runs are available for the analysis
Data replacement methods tested
  (A) missing values replaced by a threshold value
  (B) missing values replaced by last available value
Rock salt plug is “closed” by ongoing compaction if plug porosity < 0.3%
From then, brine inflow/ outflow is impossible
Nuclide transport from borehole is terminated
A
B

## Slide 12: Statistical Analyses Dose rate (wet scenario)
Very small dose rates due to early “closure” of rock salt plug
Time evolution of SRRC and R2 for the 6 model input parameters
Effect of input parameters on dose rate changes with time

## Slide 13: NRG: Generic repository design in Boom clay
HLW disposal in horizontal boreholes
Belgian ‘Supercontainer’ concept
2 COGEMA canisters per container, one container per disposal cell
Focus on: ‘abandonment scenario’
  no backfill
  no sealing of borehole
  immediate total flooding of the central field
  immediate failure of all containers
Uncertainty/sensitivity analysis: 500 PORFLOW runs

## Slide 14: Modelling of the repository
PORFLOW: multiphase fluid flow, heat and mass transport in fractured porous media
Radial 2D model
Three variable input parameters
  composition of the plug unknown; varied between concrete and clay
  diffusion constant: best guess (Boom clay) varied with factor 10
  glass dissolution rate: large uncertainties due the high pH of concrete dissolution; varied between 100 and 10’000 years

## Slide 15: Statistical Analyses - Dose rate
Dose rates are well below limits
Most of the radionuclides (>95%) diffuse into the clay
Less than 5% of the released nuclides are transported through the water-filled (“abandoned”) gallery
Time evolution of SRRC and R² for the 3 model input parameters; rank transformed data
Dependent on contributions of individual, main nuclides (79Se, 126Sn, 229Th)

## Slide 16: Findings from NRG Investigations
Methodology
  Log-transformation made output distributions more symmetric and improved (in most of the cases, but not always) the quality of regressions (larger R² values)
  Even larger R² values were obtained when the ranks were used
  The most meaningful statistical indicators were:
    R² values to see if the regression analysis is reliable
    SRRC as main sensitivity measure (easy interpretation)
Implication of uncertainty of repository safety
  Calculated potential dose rates were far below legal limits.
  The uncertainty in parameterisation was therefore assumed to be not relevant
  Clay case: the apparent diffusion coefficient Da is the most relevant parameter influencing repository safety on the long term

## Slide 17: Enresa Case
Canister failure between 20 000 and 100 000 years
A few (≤ 10) canisters failing after 100 years
Solubility limits assumed
1D transport models for bentonite and granite
Radionuclide release to a river
Exposure of men using river water for drinking and food production

## Slide 18: Correlation and regression analysis (peak doses)
Increasing the number of runs allows identifying weak influences
The threshold value above is considered statistically significant decreases with the number of runs following the “rule of thumb”
  This dependence has been observed for different statistics (not only CC/RCC)
  Non-relevant parameters can be used to generate the threshold. The resulting “empirical” threshold are in good agreement with “predicted” thresholds
200 runs
5,000 runs
25,000 runs
1,000 runs
0
0.2
0.4
0.6
0.8
1
- 0.2
- 0.8
- 0.4
- 0.6
- 1
I129
enough

## Slide 19: Derived parameters
PA experts can identify some parameters that are known to have a strong effect on doses and are a combination some random input parameters: “derived parameters”
The correlation/regression analysis shows that the derived parameters present stronger correlations with the peak doses than the random input parameters.

## Slide 20: Ranking of importance of the parameters
“In general, each measure of sensitivity will produce its own ranking of factors by importance”. Global Sensitivity Analysis. The Primer (A. Saltelli)
BUT in our particular system the different statistics identify the same set of relevant parameters with a similar ranking of importance.
This agreement provides robustness to the SA
Different statistics are complementary and give particular information
“Derived parameters” always lead the ranking

## Slide 21: GRS Case
Generic salt concept
Shaft failure scenario
Compartment model for near field
1D transport model for far field
  advection
  diffusion
  sorption
Exposure in biosphere
6 independent uncertain parameters
  Shaft permeability
  Dam permeability
  Shaft failure time
  Reference convergence rate
  Sorption in the far field
  Diluting water flow in the aquifer
85 % zero output probability!
4 samples drawn
  types: Random / EFAST
  sizes: ~ 3000 / ~ 6000

## Slide 22: Graphical SA (peak dose rate, 6054 runs)
Scatter plots
CSM plot
Cobweb plot
Rank | Input parameter
1 | Shaft permeability
2 | Ref. convergence rate
3 | Dam permeability
4 | Failure time
5 | Aquifer flow
6 | Sorption factor
Smirnov test ranking

## Slide 23: Time-dependent SA
PEAR
SPEA
Rank Transformation
Transformation
0 → 0
a → 1
big value → ~ log (big value)
Total variance
Total variance

## Slide 24: General Conclusions
The main sensitivities are identified by all SA methods
Different SA methods can yield very different results for less important parameters
Graphical methods provide a good means for a clear qualitative SA
Regression and correlation methods are easy to apply and adequate to identify the most relevant dependencies
A rank transformation improves the significance of regression and correlation methods but decreases the quantitative information
Variance-based methods (EFAST) are promising for a more sophisticated SA, but have to be applied with care
An adequate transformation can improve the robustness of variance-based methods

## Slide 25: Thank you!
Ricardo Bolado-Lavin
José-Luis Cormenzana
Jaap Hart, Thorsten Schröder
Rodolfo Avila, Robert Broed
Dirk Becker, Sabine Spießl