## Slide 1
Probabilistic Safety Assessment
Complementary PSA calculations
José Luis Cormenzana (Enresa)
Final Workshop Hohenkammer (Germany) 28-30 September 2009

## Slide 2: Work performed
Involvement of ENRESA in PAMINA Task 2.2.E
  Make a simplified PSA of the Swiss disposal concept in clay, using
    GoldSim to create the model, and
    The pdf´s provided by Nagra/Colenco
  Comparison with the results obtained by Nagra (GoldSim/Toolbox)
Five different wastes are considered:
  Spent Fuel (SF)
  Cogema HLW
  BNFL HLW
  ILW1
  ILW2
2D and 1D models are used and the results compared

## Slide 3: 2D transport model in the simplified PSA
Bentonite and clay are discretized
in 97 “mixing cells”.
Processes considered:
Diffusion
Advection
Sorption
Anion exclusion
Radioactive decay/ingrowth

## Slide 4: Results for all the wastes
Peak doses are controlled by SF
Important contribution of ILW1 at early times

## Slide 5: Comparison with Nagra/Colenco results
Simplified PSA
Nagra/Colenco PSA
Similar results are obtained
with both models (1000 runs each)

## Slide 6: SF, effect of the number of runs
Three different calculations with 1000 runs (case 1 to 3)
  The same model is used - only the parameter sampling changes
  Doses are nearly overlapped → 1000 runs are enough

## Slide 7: SF, correlation with the peak dose
Correlation coefficients obtained in the Simplified PSA are similar to those obtained in Nagra/Colenco PSA
Darcy velocity in HR
Instant Release Fraction of Iodine
Sorption Coefficient of Iodine
Diffusion coefficient of Opalinus Clay
Transport path length in Opalinus
0.514
0.308
-0.352
0.343
-0.177
Simplified
PSA
Nagra/Colenco PSA

## Slide 8: Results with 1D and 2D models
Results with 1D and 2D models are similar
  1D model leads to earlier releases and slightly higher peak doses

## Slide 9: Conclusions
Good agreement between the results of the GoldSim/Toolbox model and the simplified GoldSim model
  Calculated doses are similar
  The same input parameters are identified as relevant for the peak doses
1000 runs are enough to obtain the time evolution of the mean dose with precision
  Runtime is about 4 hours in a powerful PC (4 cores)
1D and 2D simplified models produce similar results
  1D model is conservative (earlier releases and higher peak doses)