## Slide 1
Development of a new PSA approach –
Sharing experience
Jürg Schneider (Nagra) & Team
Final Workshop Hohenkammer (Germany) 28-30 September 2009

## Slide 2: Contents
Introduction
Methodology
Requirements for the new tool
Code development
Status & outlook
Conclusions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Introduction
Demonstration of disposal feasibility for SF, HLW and ILW
Based on a site in northern Switzerland (Zürcher Weinland)
Approach to assess radionuclide release and transport: A combination of deterministic and probabilistic analyses
Deterministic analyses
  spectrum of analyses results in spectrum of consequences
  results easy to understand and easy to explain (esp. to non-specialists)
  but: unfavourable combinations of parameter values may be overlooked
Probabilistic analyses
  consequences take into account combined effects of uncertainties
  provide assurance that no unfavourable combinations of parameter values exist that can compromise safety
Starting point: Safety Case for Project Opalinus Clay
(Entsorgungsnachweis)  Nagra reports NTB 02-05, 02-06, 02-23 (www.nagra.ch)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Deterministic and Probabilistic Analyses
SF
HLW
ILW
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: PSA (distributed evolution of dose, CCDFs)
SF
HLW
ILW
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Introduction (continued)
After Project Opalinus Clay (Entsorgungsnachweis): Decision to strengthen PSA approach  Start of a PSA development project in 2005
Phase 1: Pilot Study (see next presentation)
  concluded in July 2006
  limitations of approach used in Pilot Study: simultaneous and parallel modelling of all relevant phenomena is not possible
Phase 2: Development of a probabilistic approach considering all potentially relevant phenomena (esp. role of gas)
  start in 2006
  Nagra participation in PAMINA with this project under the motto “sharing experience”
  key (starting) point: establish a process to derive a comprehensive list of relevant phenomena to be included in PSA tool
  then: develop and apply PSA tool
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Methodology
The steps
  how to develop the PSA tool
  how to manage & run the PSA tool
Philosophy
  ensure that the broad range of uncertainties is adequately captured  get the scientists directly involved in a clearly defined process
  establish such a process to derive a comprehensive list of relevant phenomena to be included in PSA tool  list of “accepted FEPs” for PSA
  develop a tool capable of simultaneously modelling all accepted FEPs and their interactions (ambitious task)
  recognise from the start that such a tool may (initially) not run sufficiently fast for large numbers of probabilistic calculations
  but: if that should turn out to be the case, then the tool could be successively simplified until it runs fast enough for PSA calculations
  advantages of such an approach
    “automatic” benchmarks on the way from “more detailed” to “more simple”
    the effects of simplifications can be monitored
    already running the tool deterministically will yield insights into the effects of simultaneous consideration of all relevant FEPs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Requirements for the new tool (1)
Development of a comprehensive list of relevant FEPs to be included
Establishment of a working group for this task (August 2006)
Specialists included experts in safety analysis, radionuclide transport modelling, gas transport modelling, waste characteristics, geochemistry, geosciences, etc.
If an identified FEP required special attention, new sub-groups with additional experts were formed to address this FEP, in some cases supported by complementary process modelling (example: FEPs No. 1.5.4: High-pH plume: sealing effect in host rock; No. 1.5.11: High-pH plume: tunnel backfill sealing effect)
10 expert meetings were held overall (documented in internal notes)
Results documented in FEP Screening Report NAB 07-38 (PAMINA RTDC2 Milestone Report M2.2.E.2)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Requirements for the new tool (2)
Development of FEP list (continued)
Step-wise procedure
  development of a broad list of potentially safety-relevant FEPs  86 potentially safety-relevant FEPs
  discussion of the potentially safety-relevant FEPs with respect to
    relevance with regard to Swiss repository types & potential host rocks
    process understanding
    evaluation of the effect of the FEP
  judgement whether or not an individual FEP should be included in the list of accepted FEPs  52 accepted FEPs to be included in the new tool
Other requirements
For each module in the suite of codes three types of requirements were defined before the start of development work
  functional requirements (related to the accepted FEPs)
  interface requirements (related to data transfer between modules)
  performance requirements (related to module performance)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Code development: Overview
Software architecture
Development needs (based on a review of the capabilities of existing codes and the requirements defined in the previous step)
  TREETOOL: developed parallel to Phase 1 for a simplified example PSA tool
  GOLDSIM probabilistic driver: operational & tested for simplified models
  IRRC: deterministic “engine” of the new PSA tool (large effort required)
    STMAN-TD: further development of existing version (time-dependent flow boundary conditions  small effort required)
    PICNIC-TD: new development needed (existing version cannot handle time-dependent flow due to solver type used  medium effort required)
    GAS MODEL (transport of volatile nuclides in the gas phase): minor development needs (simplified treatment)
    IFC: major development effort required
    Input Data Converters: significant development effort required
    Interfaces & integration of modules: development effort required
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Integrated Flow Code IFC
Development of IFC based on TOUGH2
Time-dependent two-phase flow in the near field and geosphere of a gas-generating nuclear waste repository system for SF / HLW / ILW located in a claystone host rock (Opalinus Clay)
Provides water and gas flow fields as input to subsequent radionuclide transport calculations
Numerical code
  modification of the multiphase, multicomponent simulator TOUGH2
  code modifications: (i) implementation of “accepted FEPs”; (ii) removal of processes and features that are not needed (speed!)
Model repository system (simplified representation of the repository)  computational mesh
  emplacement tunnels for SF / HLW / ILW
  engineered barriers (backfill, seals, plugs, etc.) & other underground structures
  geological structures (host rock, EDZ, confining units, local aquifers)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: IFC (continued)
Repository
layout
Equivalent conceptual repository model
IFC model
(computational
mesh)
hydro-geo-
framework
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: IFC (continued)
CPU-time-intensive tasks:
- simulating strong changes
at early times with initial
expansion of 2-phase zone
- resolving nonlinearities and
counteracting effects (early- time pressure increase combined with tunnel convergence; late-time
transient effects due to uplift)
CPU time as a function of simulation time
all FEPs included
some FEPs excluded:
- pathway dilation
- EDZ self-sealing
- tunnel convergence
- uplift
- geochemical sealing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: EDZ Converter (1)
Successive model abstraction
Combined gas/water flow
The model to our best
geoscientific understanding
The model suitable for
PA calculations (“sim.“)
Simulate pressure & flow with the CPM model – fit simplified homogeneous model  effective parameters (rEDZ , kEDZ, rel. perm., cap. pr., ...)
rEDZ
EDZ
Heterogeneous continuum
porous medium model (“CPM”)

## Slide 15: EDZ Converter (2)
water flow
gas flow
 simulated responses (pressure and gas / water flow) from the CPM model can
be used to calibrate effective parameters for a simplified homogeneous model
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Integration of modules: IRRC
Part of IFC
Part of PICNIC-TD
2
1
3
5
4
Codes
STMAN-TD
PICNIC-TD (with Gas Model)
IFC
Linkages
1 STMAN to PICNIC
2 STMAN to Gas Model
3 IFC to PICNIC
4 IFC to STMAN
5 IFC to Gas Model
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: IFC–PICNIC linkage network (h)
h: horizontal plane
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: IFC–PICNIC linkage network (v)
v: vertical plane
Results (example: Bio_WS)
Case with 36 legs, 39 nuclides & full IFC flow field (previously calculated): 40 Min.
no MD from tunnels: 8 Min.
no flow in tunnels: ~ 3 Min.
(but results very similar)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Status & outlook
Status: IRRC is up and running, but ...
  maximum version with all accepted FEPs included is relatively slow
  max. CPU time needed for IFC (~ 45 h for 1 Ma with all accepted FEPs)
  rest of IRRC calculations ~ 40 Min. with all radionuclide processes
  a number of preliminary functionality tests completed successfully
  on-going project
Outlook
  gain further experience with running full IRRC
  successively reduce number of FEPs included and continuously monitor effect on calculated releases and on CPU time needed
  build full PSA tool (GOLDSIM, TREETOOL)
  run and test PSA tool
  for operational applications
    adapt mesh (repository design has been modified in the meantime)
    implement expert elicitation process to obtain required input (scenarios, conceptual models, data (PDFs))
  in parallel: develop simple, modular PSA tools using the GOLDSIM probabilistic driver and established radionuclide release & transport codes for SF / HLW / ILW / L/ILW for first applications (on-going)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Conclusions
Development of a fully probabilistic approach started in 2006 is well under way (on-going project)
Development of FEP list and IRRC was more difficult & time consuming than originally thought (involvement of large team of experts from many disciplines; recruited as required by progress of project)
Stand-alone IRRC
  unique tool fully incorporating 52 “accepted FEPs” derived in a systematic manner
  very useful tool “in its own right”
  excellent basis for further development (key part of “full” PSA tool):
  systematic reduction of no. of FEPs included while monitoring effects on
    calculated releases
    CPU time needed
  benchmarks obtained “for free” (“maximum version”  “reduced version”)
New versions of NF code and geosphere transport code developed “on the way” (STMAN-TD, PICNIC-TD) for time-dependent flow
Simplified modular PSA tools developed in parallel for first applications
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21
Thank you!

## Slide 22: Structure of FEP List (Categories)
Environmental FEPs
  radiation-related processes
  thermal processes
  hydraulic and gas processes
  mechanical processes
  chemical and microbial processes
  flow influenced by Onsager processes
Radionuclide FEPs
  radioactive inventory and decay
  containment failure mechanisms
  radionuclide mobilisation
  transport of dissolved (non-volatile) radionuclides
  transport of volatile radionuclides (14C)
  radionuclide pathways through host rock and confining units
  radionuclide pathways through access tunnel system
  radionuclide transport influenced by Onsager processes
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Software architecture - overview
IRRC:
“Engine” of the PSA tool
(see next slide)
TREETOOL:
Handling of alternative,
mutually exclusive
scenarios /
conceptualisations
GOLDSIM:
Probabilistic driver
of IRRC
PSA Tool:
3 nested shells
Input
Processing
Output
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Software architecture - IRRC
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: IFC Mesh
36’000 grid blocks
112’000 connections
2 equations per grid block (water / gas)  72’000 non-linear equations to be solved per grid block
~ 10’000 time steps for 1 Ma (automatically adjusted)
Notes: <number>
<footer>
<header>
<date/time>