## Slide 1
Treatment of Parameter Uncertainties and
Derivation of PDFs WP 2.2.A

## Slide 2: The Modeller’s Problem
Input parameter uncertainty causes model output uncertainty
Output uncertainty has to be assessed
Parameter uncertainties have to be quantified
Model
Input
Output

## Slide 3: Types of Parameter Uncertainty
Aleatory uncertainties
  due to random influences
  cannot be reduced
Epistemic uncertainties
  due to lack of knowledge
  can be reduced by
    collecting additional data
    improving the knowledge basis
    changing concept details
Types of uncertainties are often not uniquely distinguishable
Most uncertainties have characteristics of both types
Epistemic character is normally more important
All parameter uncertainties are handled as if they were epistemic

## Slide 4: How to Deal with Parameter Uncertainty?
Identify the uncertainties most relevant for the model
Sensitivity analysis, screening
  How sensitive is the model to parameter variations?
Uncertainty analysis
  How uncertain are the model results in view of the parameter uncertainties?
Deterministic and probabilistic methods are available
Proper quantification of the uncertainties is necessary
  Minimum - maximum interval
  Probability Density Function (PDF)

## Slide 5: Questions Addressed in PAMINA
Which of the parameter uncertainties are worth being investigated in a probabilistic study?
Which influence have the shape and parameters of the selected PDF to the uncertainty of the model results?
How should one proceed to quantify the existing knowledge and to establish PDFs?
How should one proceed to improve and assess the knowledge basis by means of expert elicitation?
How can PDFs be fitted to given data or adapted to improved knowledge?

## Slide 6: Important or Less Important Parameters?
Finnish KBS3 concept
Deterministic calculations carried out by VTT
Release of individual radionuclides analysed
Several parameters varied between estimated upper / lower limits:
  Near field
    Effect of defect size, source term and solubility limit
    Effect of near field flow rates
    Effect of retardation parameters
  Far field/geosphere
    Effect of transport parameter u
    Set of nuclides analysed: C-14, I-129, Cs-135, Ra-226, Pa-231
Exercise shows how interesting parameters can be identified

## Slide 7: Probabilistic Analysis: Influence of PDF Shape
Work performed by BEL V
Objective: assess the influence of an arbitrary use of PDFs on the model output
Belgian disposal system in Boom clay
Simple representative 2D-Model for contaminant transport from a point source
Studied output:
  Maximum activity flux
  Time of maximum activity flux
Simple SA concept:
  MELODIE Code (IRSN)
  Apply 6 PDFs to 2 key parameters for iodine:
    molecular diffusion coefficient d,
    porosity ω
  10 000 runs using LHS for each pair of PDFs,
  Analyse the combined influence of the PDFs of parameters on the global performance of the system
2 Scenarios: reference / altered

## Slide 8: Results for Altered Scenario
Influence of IPDFs remains unpredictable in the general case and conservative assumption for IPDFs is not possible without a dedicated study.
From a TSO point of view an arbitrary choice of IPDF without any guarantee of conservatism is not acceptable.
Time of maximum iodine flux
Maximum iodine flux
Conclusion: Shape of PDF is Essential!

## Slide 9: How to Determine PDFs?
Chart: 
?
??
???

## Slide 10: Transforming Knowledge to PDFs
Intentions
  Avoiding “wild guess” of PDF
  Urging the modeller to think
  Reducing subjectivity
  Generating traceability
Procedure should be as unique as possible
Knowledge
Data
Data
Data
Kwnldg
Data
Data?
Filter
Data
Data
Knowledge
Procedure
PDF

## Slide 11: Procedure for Evaluating the Knowledge Basis
Procedure developed by GRS
Collecting of information from different sources
Elimination of questionable information or data
Assessment of information quality
  Level 3: Measurements
  Level 2: Model representations
  Level 1: Analogies
  Level 0: Plausibility limits
Combination of data or information of same level
  Expert judgement necessary
Use two highest available levels and add their level numbers
  6 possible cases
Instructions for PDF derivation for each case

## Slide 12: Procedure for Evaluating the Knowledge Basis
data set 1
data set 3
data set 4
data set 5
data set 2
Step 1: Identification of data sets to be used
data set 2
data set 1
data set 3
Level 3:
Level 2:
Level 1:
data set 5
Step 2: Assessment of quality level
Level 0:
Step 3: Assessment of information
data set 1
data set 3
weight x
weight y
PDF derivation
data set 5 L2
combined data set L3
Case 5
Expert Judgement
Measurements
Models
Analogies
Plausibility limits

## Slide 13: Finding the Right PDF
Case 0: Nothing more than a plausibility interval
  No values should be preferred against others
  Use uniform distribution between interval boundaries
Case 1: Analogy, supported by plausibility limits
  Derive PDF from analogy
  Re-calibrate PDF using plausibility limits
Case 2: Model representation, supported by plausibility limits
  Derive PDF from the model
  Calibrate using plausibility limits
Case 3: Model representation, supported by analogy
  Derive PDF from the model
  Transfer PDF to analogy situation and calibrate
  Re-transfer PDF to actual situation

## Slide 14: Finding the Right PDF
Case 4: Measured data, supported by analogy
  Is the amount of measured data sufficient for deriving a PDF?
    Yes: Do it! Use the analogue for confirmation or tuning
    No: Derive PDF from the analogue Use measured data for calibration
  The situation can even become more problematic
    Expert judgement necessary
    Uniform or triangular distribution may be the best choice
Case 5: Measured data, supported by model
  Derive PDF from the model
  Calibrate PDF using measured data
  Do they fit together?
    Yes: Be happy!
    No: Expert judgement necessary Disregarding the less reliable information leads to a lower case

## Slide 15: PDF Derivation From Given Data
Problem: Deriving a PDF from a set of data points
Are there sufficient data to derive a PDF?
  Yes: How to proceed?
    Proposal by NRI: PFD derivation tool
  No: What can be done?
    Stylised PDF approach proposed by GRS
    Fuzzy number uncertainty description proposed by NRI
How can a “generic” PDF be calibrated with given data?
  Bayesian approach proposed by Facilia
Chart: 
?

## Slide 16: General procedure for treating parameter uncertainty Proposal by NRI
Mathematical procedure for treating parameter uncertainty on the basis of available data
All necessary tools for working with the proposed procedure built by NRI
Describe parameter uncertainties by a fuzzy number.
Describe parameter uncertainties by probability density function (PDF).
Simulate model using Monte Carlo method.
Simulate model using the transformation method.
Express model output uncertainties by PDF.
Express model output uncertainties by a fuzzy number.
THE SUBJECTIVE INTERPRETATION OF PROBABILITY
Are there enough data to define statistically representative probability distributions?
THE FREQUENTIST INTERPRETATION OF PROBABILITY
YES
NO

## Slide 17: PDF Derivation Tool (NRI)
A graphical user interface for fitting PDFs to data. The program makes easy to follow a step-wise process :
Construct empirical distribution.
Construct probability plot.
Perform maximum likelihood estimation
Perform nonlinear regression.
Choose best acceptable fit.

## Slide 18: Modelling uncertainty by use of fuzzy set theory (NRI)
Condition: The available basis of data is poor
Model an uncertain parameter as a fuzzy number
Apply transformation method to propagate the fuzzy input through the computational model
  Implemented into the computational model of radionuclide transport in the near-field region of a high level nuclear waste repository
  Created in the GoldSim programming environment
  Performance of the transformation method demonstrated
Conclusion: it is practically feasible to treat uncertainties in parameters of a complex computational model by the fuzzy set theory

## Slide 19: Bayesian updating of PDFs (Facilia)
Combining a priori knowledge with experimental data using Bayesian methods
Three methods demonstrated, each with its own field of application:
  I. Direct updating
  II. Hierarchical updating
  III. Updating of model parameters
Normal or log normal distributions of the parameters are assumed.
I. Direct updating
Used when the a priori knowledge is a generic PDF or a PDF of an analogue parameter
The posterior PDF is a weighted combination of the a priori PDF and a specific PDF, taking into account total variability and differences between PDFs.

## Slide 20: Bayesian updating of PDFs (Facilia)
II. Hierarchical updating
Useful when data for several analogue parameters are available, but some have little data and others have more data. The estimate of the PDF for parameters with less data will be improved by parameters that have more data.
The prior distribution is not specified explicitly for a parameter but estimated from the available data of the analogue parameters.
Given an updated hierarchical model, the prediction of probable outcomes for unobserved analogues is possible.
III. Updating of model parameters
Decreasing the uncertainty of model parameters by taking a priori uncertainty into account.
The updating of the coefficients of a regression model was demonstrated. The a priori uncertainty of the coefficients is updated as measurements becomes available.

## Slide 21: Summary and Lessons Learnt
Deterministic sensitivity analysis is an adequate tool for identifying relevant uncertainties
Uncertainties should be quantified in a traceable manner
A procedure for dealing with a given data and knowledge situation was proposed
A proper selection of Input PDFs is essential for convincing probabilistic uncertainty and sensitivity analysis
PDFs can be derived from data sets if they are large enough
  PDF derivation tool
Generic PDFs can be calibrated or updated using available data
  Bayesian approach
Poor data situations require specific measures
  Fuzzy number approach
  Stylised PDF generation

## Slide 22: Thank you!
Henrik Nordman
Olivier Destin, Olivier Smidts
Rodolfo Avila, Kristofer Stendberg
Aleš Vetešník
Dirk-A. Becker, Eckhard Fein, Jörg Mönig